NOTE:  This Section 01120 "Alteration Project Procedures” includes requirements for performing alteration and renovation Work applicable to all sections of involved in the alterations and procedures for salvageable materials.  Coordinate this section with Division 2 “Selective Demolition” or “Minor Demolitions” or any other sections from Divisions 2 through 16 relating to alteration and renovation Work should specifically reflect this Section.  This Section requires close coordination with drawings and should define scope of Work in the fullest possible detail.  General, broad statements in his section may be interpreted to require more Work than intended, adding to the construction costs unnecessarily, and must be carefully to reflect specific project requirements, or delete them if they do not apply.

The header and footer for each page of the Project Manual shall match the format, font (Times New Roman), size (11 pt), font style (BOLD & CAPITALIZED) and line boarders, of the header and footer shown herein.. The header of each page shall contain the Section Number, the Section Title, and the page number & number of pages as shown herein. The footer shall contain the project number in the right hand side as shown herein, including the Table of Contents.  Division 0 and 1 contain a revision date in the left side of the footer This date is to remain as it is for Department informational purposes only and should not be altered by the Architect/Engineer.

DO NOT include Paragraphs or parts of Paragraphs in the project manual, which have no applicability to the specific project.  KEEP IN NUMERICAL SEQUENCE, If A PART IS NOT USED OR ELIMINATED THEN RENUMBER THE FOLLOWING SECTIONS.  IF A PART IS NOT APPLICABLE TO A SPECIFIC PROJECT THEN DESIGNATE IT AS (NOT APPLICABLE).  Also, please review the General Conditions carefully and coordinate the requirements of those Articles including the Definitions.

# PART 1 - GENERAL

## 1.1	RELATED DOCUMENTS

### A.	Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections, apply to this Section.

## 1.2	SUMMARY

### This Section includes administrative and procedural requirements for performing alteration and renovation Work.

### Related Sections:  The following Sections contain requirements that relate to this Section:

NOTE:  Include one or more of the following referenced sections are utilized.

#### Division 1 Section 01040 "Coordination" for procedures for coordinating cutting and patching with other construction activities.

NOTE:  Edit and or delete the subparagraph below if cutting and patching is not required and the " cutting and patching " section is not used.

#### Division 1 Section 01045 "Cutting and Patching" for procedures for cutting and patching.

NOTE:  Insert the name of the division 2 demolition section in paragraph below.  Delete the subparagraph below if demolition is not required and a demolition" section is not used.

#### Division 2 Section       for demolition of selected portions of the building for alterations.

NOTE:  The subparagraph below is appropriate to items in many other sections..

#### Refer to other Sections for specific requirements and limitations applicable to performing alteration Work with individual parts of the Work.

NOTE:  Delete the subparagraph below if alteration and renovation Work requirements by mechanical and electrical trades are not required.

##### a.	Requirements of this Section apply to mechanical and electrical installations.  Refer to Division 15 and Division 16 Sections for other requirements and limitations applicable to renovations Work by mechanical and electrical installations.

# PART 2 - PRODUCTS

## PRODUCTS FOR PATCHING AND EXTENDING WORK

### New materials:  As specified in product sections;  match existing Products and Work .for patching and extending Work.

### Type and Quality of Existing Products:  Determine by inspecting and testing Products where necessary, referring to existing Work as a standard.

## SALVAGEABLE MATERIALS

NOTE:  On alteration, renovation, demolition and replacement Work, the ownership of the salvageable materials should be investigated and a statement as to whose property it becomes should always be included in the Specifications.  Edit, and add or delete from examples of salvageable items listed below.   If the State or an Agency is to salvage any items then include the location where agency will storage is to be provided.

### The Contractor shall be responsible for removing the following salvageable items from premises and transporting said items to       on      , CT      .

#### Equipment:

#### Windows:

#### Doors:

#### Door Hardware:

#### Fixtures:

#### Art:

NOTE:  Insert the name and location of the agency facility where salvageable are to be stored.  Also insert the name the agency whose personnel responsible for directing contractor where salvageable materials are to be stored.

### The Contractor shall notify the Construction Administrator in writing (7) seven Calendar Days prior to removing all salvageable items from the existing alteration project location and unloading all salvageable items at      ,      , Connecticut       and store items in the appropriate location as directed by       personnel.

# PART 3 - EXECUTION

## 3.1	INSPECTION

### General;

#### Verify that demolition is complete and areas are ready for installation of new Work.

#### Beginning of restoration Work means acceptance of existing conditions.

NOTE:  Include the following Sections and paragraphs for all facilities that have Work Involving Lead Containing Material.  Edit and or delete paragraphs as required for specific project.

### Project Procedures for Work Involving Lead Containing Material (LBP):

#### Exposure levels for lead in the construction industry are regulated by 29 CFR 1926.62.  Construction activities disturbing surfaces containing lead-based paint (LBP) which are likely to be employed, such as sanding, grinding, welding, cutting and burning, have been known to expose workers to levels of lead in excess of the Permissible Exposure Limit (PEL). Conduct demolition and removal Work specified in the technical sections of this specification in conformance with these regulations.  In addition, construction debris/waste may be classified as hazardous waste.  Disposal of hazardous waste material shall be in accordance with 40 CFR Parts 260 through 271 and Connecticut Hazardous Waste Management Regulations Section 22a-209-1; 22a-209-8(c); 22a-449(c)-11; and 22a-449(c)-100 through 110.

NOTE:  Include the following paragraph for all facilities in which children under six years old reside.

#### The Contractor's Work shall be based on a child under the age of six (6) in residence; the Work shall also be in accordance with Connecticut Regulations Section 19a-111-1 through 11.

NOTE:  Include the following paragraph for all facilities constructed prior to 1978.

#### This facility was constructed prior to 1978 and is likely to have painted surfaces containing lead-based paint.

NOTE:  DPW Project Managers should make arrangements for lead inspections by submitting requests to the DPW Asbestos Management Unit.  When the facility has been inspected for the presence of lead-based paint, insert the following paragraph.

#### Testing for lead-based paint has been conducted at the facility scheduled for renovation, demolition, reconstruction, alteration, remodeling, or repair.  Results of the LBP testing are for information purposes only.  The results are in this Project Manual.  Under no circumstance shall this information be the sole means used by the Contractor for determining the extent of LBP.  The Contractor shall be responsible for verification of all field conditions affecting performance of the Work.

NOTE:  Include the following Sections and paragraphs for all facilities in reference to Asbestos Containing Material (ACM) disclosure and removal..

### Project Procedures for Work Involving Asbestos Containing Material (ACM)

#### The Owner is responsible for abating all ACM that is visible and accessible.  This is to be accomplished through a separate project prior to the start of the renovation project.  In demolition projects, every attempt should by the owner to remove all ACM.

NOTE:  An Owner 24 hour response and testing time and (7) seven Calendar Days abatement time is included in the paragraph below, if different response time is required, edit and insert a reasonable time period into paragraphs.  The State cannot guarantee any time period for inspection, testing and removal (if necessary).  Edit and or delete paragraphs as required for specific project.

#### If the Contractor should encounter any material suspect or known to contain ACM, he should immediately notify the Construction Administrator of same.  It is the State’s responsibility to have the material tested and abated (if necessary).  The Owner will respond within (24) twenty-four hours after receiving the Contractor’s written request to the Construction Administrator for testing the suspect material.  The Owner will abate ACM (if necessary) within a reasonable time period, i.e. with (7) seven Working Calendar Days.

#### Testing for asbestos has been conducted at the facility scheduled for renovation, demolition, reconstruction, alteration, remodeling, or repair.  Results of the asbestos testing are for information purposes only. The results are in this Project Manual.  Under no circumstance shall this information be the sole means used by the Contractor for determining the extent of asbestos.  The Contractor shall be responsible for verification of all field conditions affecting performance of the Work.

### Project Procedures for Work Involving Products Containing Persistent Bioaccumulative Toxic Chemicals” (PBT’s) such as Polychlorinated Biphenols (PCB’s), Di-2-ethylhexyl Phthalate (DEHP), and Mercury:

#### The Contractor is responsible for abating all PCB’s, DEHP, and mercury prior to the start any work involving construction, renovation or demolition (if necessary).

#### Exposure Levels for  Products Containging Persistent Bioaccumulative Toxic Chemicals (PBT’s) such as PCB’s. DEHP, and mercury in the construction industry is regulated by 29CFR1910.1200 and 29CFR1926.28 et. al.  Construction, renovation or demolition activities disturbing Products Containing Persistent Bioaccumulative Toxic Chemicals” (PBT’s) such as PCB’s and DEHP which are likely to be employed.  These materials include but are not limited to fluorescent light fixture & exit sign, ballasts, high density discharge (HID) lamps , and certain types of construction products containing vinyl, and  mercury containing electrical switches and thermostats.  These activities may expose workers in excess of the respective Permissible Exposure Limit (PEL).  Conduct demolition and removal Work specified in the technical sections of these specifications in conformance with these regulations.  In addition construction debris/waste may be classified as hazardous waste.  Disposal of all hazardous materials shall be in accordance with but not limited to 40CRF Parts 761 Subpart K, 761, and 761.65 and the Connecticut General Hazardous Waste Statute Sec. 22a-454.

#### A Survey for Products Containing Persistent Bioaccumulative Toxic Chemicals (PBT’s) such as PCB’s, DEHP and Mercury has NOT been conducted at the facility.  Examples include but are not limited to fluorescent light fixture & exit sign, ballasts, high density discharge(HID) lamps , and certain types of construction products containing vinyl, and  mercury containing electrical switches and thermostats.  It is the Contractors responsibility for verification of all material and field conditions prior to construction, renovation, and demolition that may affect the performance of their Work.

### See also General Conditions Article 23 “Cutting, Fitting, Patching and Digging.”

## 3.2	PREPARATION

### Cut, move, or remove items as are necessary for access to alterations and renovation Work.  Replace and restore at completion.

### Remove unsuitable material not marked for salvage, such as rotted wood, corroded metals, and deteriorated masonry and concrete.  Replace materials as specified for finished Work.

### Remove debris and abandoned items from area and from concealed spaces.

### Prepare surface and remove surface finishes to provide for proper installation of new Work and finishes.

NOTE:  Include salvageable items in the paragraph below if project includes salvageable materials.  Edit and delete salvageable items if none.

### Close openings in exterior surfaces to protect existing Work and salvage items from weather and extremes of temperature and humidity.  Insulate ductwork and piping to prevent condensation in exposed areas.

## 3.3	INSTALLATION

### Coordinate Work of alterations and renovations to expedite completion, and if required sequence Work to accommodate Owner occupancy.

NOTE: Subparagraphs may need to reference Section 01045 “Cutting and Patching”.

### Remove, cut and patch Work in a manner to minimize damage and to provide restoring Products and finishes to original and or specified condition in accordance with Section 01045 “Cutting and Patching”.

### Refinish visible existing surfaces to remain in renovated rooms and spaces, to specified condition for each material, with neat transition to adjacent finishes in accordance with Section 01045 “Cutting and Patching”.

NOTE:  Edit the following paragraph and delete inapplicable examples.  Closely coordinate with drawings and with individual product specification sections.

### In addition to specified replacement of equipment and fixtures, restore existing plumbing, heating, ventilation, air conditioning, electrical, systems to full operational condition.

### Recover and refinish Work that exposes mechanical and electrical Work exposed accidentally during the Work.

### Install Products as specified in individual sections.

## 3.4	TRANSITIONS

### Where new Work abuts or aligns with existing, perform a smooth and even transition.  Patch work to match existing adjacent Work in texture and appearance.

### When finished surfaces are cut so that a smooth transition with new Work is not possible, terminate existing surface along a straight line at a natural line of division and make recommendation to Architect/Engineer.

## 3.5	ADJUSTMENTS

### Where removal of partitions or walls result in adjacent spaces becoming one, rework floors, walls, and ceilings to a smooth plane without breaks, steps, or bulkheads.

NOTE:  Edit the following paragraph and insert appropriate dimensions as applicable to project.  Closely coordinate with drawings and with individual product specification sections. Standard is indicated- if closer tolerance is required- modify the standard.

### Where a change of plane of ¼ inch in (12) inches or more occurs, request recommendation from Architect/Engineer for providing a smooth transition.

### Trim existing doors as necessary to clear new floor finish.  Refinish trim as required.

### Fit Work at penetrations of surfaces as specified in Section 01045 “Cutting and Patching”.

## 3.6	REPAIR OF DAMAGED SURFACES

### Patch or replace portions of existing surfaces that are damaged, lifted, discolored, or showing imperfections.

### Repair substrate prior to patching finishes.

## 3.7	FINISHES

### Finish surfaces as specified in individual Product sections.

### Finish patches to produce uniform finish and texture over entire area.  When finish cannot be matched, refinish entire surface to nearest intersections.

## 3.8	CLEANING

NOTE: Subparagraph needs to reference ”Cleaning” in Section 01500 “Construction Facilities and temporary Controls”.

### In addition cleaning specified in Division 1 Section 01500 “Construction Facilities and Temporary Controls”, clean Agency occupied areas of Work

END OF SECTION 01120