To print this document the show/hyde symbol (¶) must be off – this will enable the document to indicate the correct number of total pages.

NOTE TO ARCHITECT/ENGINEER & PROJECT MANAGER:

Division 1 Sections are the organizational key of the Project Manual.  All revisions to this Division are the responsibly of the Architect/Engineer.  Division 1 must be closely coordinated with Division 0, Division 2 through 17, the Drawings and the DPW Bid Data Sheet (to be filled out by the Architect/Engineer for bidding).

DO NOT include Paragraphs or parts of Paragraphs in the project manual, which have no applicability to the specific project.  KEEP IN NUMERICAL SEQUENCE, If A PART IS NOT USED OR ELIMINATED THEN RENUMBER THE FOLLOWING SECTIONS.   IF A PART IS NOT APPLICABLE TO A SPECIFIC PROJECT THEN DESIGNATE IT AS (NOT APPLICABLE).  Also, please review the General Conditions carefully and coordinate the requirements of those Articles including the Definitions.

The header and footer for each page of the Project Manual shall match the format, font (Times New Roman), size (11 pt), font style (BOLD & CAPITALIZED) and line boarders, of the header and footer shown herein.. The header of each page shall contain the Section Number, the Section Title, and the page number & number of pages as shown herein. The footer shall contain the project number in the right hand side as shown herein, including the Table of Contents.  Division 0 and 1 contain a revision date in the left side of the footer This date is to remain as it is for Department informational purposes only and should not be altered by the Architect/Engineer.

## 01000	WORK COVERED BY CONTRACT DOCUMENTS

### Project Number       is entitled      .  It is to be located in      , Connecticut.  It is to be completed and ready for use by the Owner and Agency within the Contract Time specified in Section 00020 Bid Proposal Form.

### The Project Description:

NOTE:  Include an abbreviated summary of major items of work for the project described above in the above paragraph.  An Example of new construction follows, edit as necessary.  Change for Renovation Work or a combination of types of Work.

#### Construction of a building of approximately       gross square feet.

#### The building is new and shall be constructed of materials that include but are not limited to the following:  The structure shall consist of      .  Exterior wall construction shall consist of      .  Roof construction shall consist of      .  Foundations shall consist of      .  Interior finishes include      .  Floor coverings include      .  Ceilings shall be      .

NOTE:  Select correct definition below that applies and delete the other.

#### This Project Exceeds the Threshold limits as defined by the Connecticut General Statutes.

OR

#### This Project does not Exceed the Threshold Limits as defined by the Connecticut General Statutes.

### Project Location:  The      , located in      , Connecticut.

## 01001	OWNER AND AGENCY

### A.	Owner:  The Owner is the Department of Public Works, State of Connecticut.

#### 1.	The authorized representative for the Owner is      , Project Manager.  The Project Manager is located at Room      , 165 Capitol Avenue, Hartford, CT, 06604.  Phone:      ;  Fax:      ;  E-mail:      .

NOTE:  For all projects, identify the name, location and phone/fax numbers of the Project Manager, authorized to perform this function.  See Article 25 “All Work subject to Control of the Commissioner” in the General Conditions for the authority of the Project Manager.

##### The Project Manager is the authorized representative for the Department of Public Works Commissioner to act in matters involving revoking, altering, enlarging or relaxing any requirement of the contract documents.

### Agency:  The Agency is      .

NOTE:  Identify the name and location of the Agency.

#### 1.	The Agency Representative is      .  The Agency Representative’s title is       .  The Agency Representative is located at      . Connecticut,      .  Phone:      ; Fax:      ;  E-mail:      .

NOTE:  Identify the name and location of the Agency Representative.

#### The Agency Representative has the administrative authority for the facility and or site where the work is being performed but does not have the authority to change the contract documents or direct the contractor.

## 01002	ARCHITECT AND ENGINEER:

NOTE:  Identify the names of Architect or Engineer for all projects.  This section uses the term Architect and Engineer.  Change this term as necessary to match the actual term used to identify the design professionals appropriate for the project  and as defined in the General and Supplementary Conditions.

### The Architectural Firm is      , and is located at      ,      ,     . The Architect representing the firm for this project is      .  Phone:      ;  Fax:      ;  E-mail:      .

#### The Architect and Engineer or their accredited representative is referred to in the Contract Documents as "Architect" or "Architects" or "Engineer" or "Engineers" or by pronouns which imply them.  As information for the Contractor, the Architect’s or Engineer's status is defined as follows:

#### The Architect and Engineer will not make interpretations or decisions directly to the Contractor.  All interpretations or decisions will be conveyed through the Construction Administrator.

#### As the authorized representative of the Department of Public Works Commissioner, the Architect and Engineer is responsible for review of shop drawings, materials, and equipment intended for the work, in accordance with the "General Conditions", and the "Supplementary Conditions”.

#### Wherever the Architect or Engineer is mentioned in the documents in connection with an administrative function, it shall include the Construction Administrator in that function except for shop drawings.

## 01003 	CONSTRUCTION ADMINISTRATOR:

NOTE: Identify the named Construction Administrator for all projects.  See Article 26 “Authority of the Construction Administrator” in the General Conditions for the authority of the Construction Administrator.

### The Construction Administrator is      , and is located at      , Connecticut,      . Phone:      ; Fax:      ; E-mail:      .

##### The Construction Administrator is referred to in the Contract Documents as "Construction Administrator" or "Construction Manager" or by pronouns which imply it.  All communications concerning the project will be directed through the Construction Administrator or a designated representative(s).

##### As information to the Contractor, the Construction Administrator’s status is defined as follows:

##### The Construction Administrator is the Owner's Agent who will, among other thing’s, monitor the General Contractor's performance, scheduling and construction, process shop drawings, material, and equipment submittals, review and process periodic billings, review and recommend cost changes.

##### The Construction Administrator will process all requests for information, interpretations and decisions regarding the meaning and intent of the Contract Documents, consulting with appropriate parties prior to rendering the interpretations or decisions to the Contractor.  All such requests and replies shall be in writing.

## 01010	SUMMARY OF WORK

NOTE:  Insert summary of work here.  Examples of types of work are shown below.  EDIT EXAMPLES BELOW AS REQUIRED FOR THIS SPECIFIC PROJECT.

### Summary of Work includes but is not limited to the following:

#### Sitework, Landscaping, Site Utilities;

#### Cast-in-Place Concrete, Architectural Precast Concrete;

#### Masonry;

#### Structural Steel, Miscellaneous Metals;

#### Rough Carpentry, Architectural Woodwork, Laminate Clad Casework;

#### Waterproofing, Insulation, Sprayed-on Fireproofing, Firestopping, Roofing, Sheet metal, and Joint Sealants;

#### Doors and Frames, Overhead Doors, Aluminum Windows, Hardware, and Glazed Aluminum Curtain Wall;

#### Drywall, Floor Coverings, Acoustical Ceilings, and Painting;

#### Visual Display Boards, Toilet Compartments, Louvers and Vents, Wall Surface Protection Systems, Signage, Lockers, Fire Extinguishers, and Toilet Accessories;

#### Projection Screens, Loading Deck Equipment, Dark Room Equipment, Laboratory Furnishings, Fume hoods, Fittings and Fixtures, and Equipment;

### The Contractor will include in his bid, all items required in order to carry out the intent of the work as described, shown and implied in the Contract Documents.

### It shall be the Contractor's responsibility upon discovery to immediately notify the Construction Administrator, in writing, of errors, omissions, discrepancies, and instances of noncompliance with applicable codes and regulations within the documents, and of any work which will not fit or properly function if installed as indicated on the Contract Documents.  Any additional costs arising from the Contractor's failure to provide such notification shall be borne by the Contractor.

NOTE:  Identify type of contract for this project as state in the Bid proposal Form.

### The Work will be constructed under a single lump.

### Work Sequence - Phase(s):

NOTE: Example:  Amplify paragraphs below as necessary. Revise to suit actual project conditions. Insert number of Phases and completion date(s) as required.

#### The entire Project shall be constructed in       Phase(s).  Work of these Phase(s) shall be substantially complete, ready for occupancy within       Calendar Days of commencement of the Work.

NOTE:  Example:  Insert Phase number and brief description of the intent of the each Phase as required.  Repeat as required for each Phase.

#### Phase       shall include the following portions of work, including all labor and material, shown on the drawings and/or as specified hereinafter. Work of this Phase shall be substantially complete, ready for occupancy within       Calendar Days of commencement of the Work .  The intent of this Phase is to       and includes but is not limited to the following:

#### Phase       shall include the following portions of work, including all labor and material, shown on the drawings and/or as specified hereinafter. Work of this Phase shall be substantially complete, ready for occupancy within       Calendar Days of commencement of the Work .  The intent of this Phase is to       and includes but is not limited to the following:

## 01011	EXAMINATION OF SITE

### It is not the intent of the Documents to show all existing conditions.  All contractors are advised to visit and examine the site with the Construction Administrator prior to submitting bids.

### Contractors should investigate and satisfy themselves as to the conditions affecting the work, including but no restricted to those bearing upon transportation, disposal, handling and storage of materials, availability of labor, water, electric power, uncertainties of weather, roads or similar physical conditions of the ground, the character of equipment, and facilities needed preliminary to and during the prosecution of the Work. The Contractor should further satisfy himself as to the character, quality, and quantity of surface and subsurface materials or obstacles to be encountered insofar as this information is reasonably ascertainable from an inspection of the site, as well as from information presented by the Contract Documents.  Any failure by the Contractor to acquaint himself with the available information shall not relieve him from the responsibility for estimating properly the difficulty and cost of successfully performing the Work.

NOTE:  Revise the sentence below for Geo-Technical Reports, Boring Logs, and Boring Location Plans as appropriate for the project or delete entirely if not required

### Review Of Geo-Technical Reports and Boring Logs are contained in a separate Volume of this Project Manual, the Boring Location Plans are in the Contract Documents.

### Pre-Bid Conference:

#### A Pre-Bid Conference and tour of the site will be conducted as scheduled in the Invitation to Bid.  This scheduled conference is the only official opportunity for the bidders to tour the site with the Owner, Architect, Engineer, Construction Administrator, and Agency.

## 01012	PROJECT DOCUMENTS

### The Specifications and Drawings are intended to describe and illustrate the materials and labor necessary for the work of this Project.

### Throughout the Technical Specifications, the Connecticut Department of Transportation Standard Specifications for Roads, Bridges, and Incidental Construction Form 814A, current addition including any interim and supplemental specifications are referenced.  Where so referenced the requirements set forth therein are applicable and made a part hereof Copies of Form 814A are available from the Connecticut Department of Transportation at a nominal charge.

## 01013	DOCUMENTS FURNISHED

Insert number of sets; minimum of 10 sets for small projects . This is a guideline, the A/E and Project Manager shall determine the number by the number of sub-contractors that will be involved with the job.

### The General Contractor will be given       sets of the Contract Documents on or about the time of execution of Contract, free of charge. If additional copies are wanted, they will be available at the direct additional cost of their reproduction, to the contractor.

Delete item B Below if project does not warrant CADD Disks.

### The Contractor shall receive one (1) set of AutoCAD compatible (latest version) Floor Plans on disks at no cost on or about the time of execution of the Contract from the Architect.  Additional sets of AutoCAD compatible (latest version) Floor Plans on disks from the Architect at the cost of their reproduction, to the contractor.

## 01014	CONTRACTOR'S USE OF PREMISES

### The Contractor shall confine his operations, including storage of apparatus, equipment and materials to the contract limit lines as directed by the Construction Administrator.

### The areas and/or spaces, including their access, shall be maintained free and clear throughout the contract term.

### Parking for Contractor's employees will be limited to an area (or areas) designated by the Construction Administrator. The Contractor may be required to provide identification stickers for employees' cars.

## 01015	OCCUPANCY REQUIREMENTS

NOTE:  This Article contains paragraphs describing occupancy of the project during construction.  It also describes partial occupancy before substantial completion.  Modify as necessaryf or size & scope of project

NOTE:  Retain paragraphs below when the Agency will occupy the premises during construction.  Modify as necessary.

### Full Agency Occupancy During Construction:  The Agency will occupy the site and existing building during the entire construction period.  Cooperate with the Agency during construction operations to minimize conflicts and facilitate Owner usage.  Perform the Work so as not to interfere with the Agency's operations.

#### Provide adequate building and fire code egress from the buildings during the renovation process.  The Contractor will be responsible to maintain and protect egress ways during the construction sequence per the design as supplied by the Architect.  Contractor shall be responsible for preparing egress plans for Owner approval and for Office of State Building Official and Office of State Fire Marshal for approval if required.

NOTE:  Retain paragraph below when the Agency might occupy completed portions of the building prior to substantial completion.  Modify to suit project requirements.

### Partial Agency Occupancy:  The Agency reserves the right to occupy and to place and install equipment in completed areas of the building prior to Substantial Completion, provided such occupancy does not interfere with completion of the Work.  Such placing of equipment and partial occupancy shall not constitute acceptance of the total Work.

#### Should it become necessary or advisable, as the work nears final completion, for the Agency to occupy a portion of the building prior to final acceptance, the Contractor shall cooperate in completing such areas and making same accessible.

#### The Construction Administrator will determine whether such occupancy or use is possible and, if so, will make arrangements for holding a job inspection with the Project Manager, Agency Representative, Architect and General Contractor.

#### A comprehensive list of items to be completed or corrected as issued by the General Contractor, together with the status of completion and terms of occupancy, will be forwarded to the Project Manager and the Architect by the Construction Administrator.  A letter will be issued by the Project Manager and Architect to Construction Administrator granting such occupancy and will state the terms and conditions of occupancy.

#### Prior to partial Agency occupancy, mechanical and electrical systems shall be fully operational.  Required inspections and tests shall have been successfully completed.  Upon occupancy, the Agency will operate and maintain mechanical and electrical systems serving occupied portions of the building.

NOTE.  For Paragraph below review Section 01027 “Application for Payment” that also uses “Certificate of Substantial Completion” for Final Payment, carefully coordinate the sections.

#### The Architect will prepare a “Certificate of Substantial Completion” for each specific portion of the Work to be occupied prior to Agency occupancy.  Use the “Certificate of Substantial Completion” form as required by the Owner.

NOTE:  Retain either paragraphs dependent on whether project is non threshold limit building or building exceeds threshold limits  Agency will occupy portions of building during construction.  Delete non-applicable paragraph. For projects that do not exceed the threshold limit:

#### The Project Manager will request a signed “Certificate of Compliance” from Commissioner of the Department of Public Works, Architect, and Contractor, if required.

OR for projects that exceed the Threshold limit:

#### The Project Manager will request a signed “Certificate of Compliance” from the , Architect, and Contractor, and forward the Certificate to the Office of State Building Inspector for a Certificate of Occupancy and obtain the same after his review and approval.

NOTE:  Retain paragraphs below to describe procedures and requirements necessary before partial occupancy of portions of the project. Modify as necessary.

#### A letter from the Project Manager to the Agency Representative with copy to the General Contractor granting occupancy will state the terms and conditions of occupancy and that fire insurance coverage has been requested, the effective date of which will indicate to the Contractor that he may cancel fire insurance coverage for that portion of the project.

#### Upon occupancy, the Agency will assume responsibility for maintenance and custodial service for occupied portions of the building.

#### Work after Partial Agency Occupancy:

##### For all work to complete the area occupied, warranty work, the balancing and commissioning of systems, repair of latent defects and adjustments after partial occupancy, the contractor is responsible for all costs associated with working in occupied buildings.

NOTE:  Retain paragraphs below when the Agency will occupy building after construction.  Modify as necessary.

### Agency Occupancy:

#### The Construction Administrator will determine whether such occupancy is possible and, if so, will make arrangements for holding a job inspection with the Project Manager, Agency Representative, Architect and General Contractor.

#### A comprehensive list of items to be completed or corrected as issued by the General Contractor, together with the status of completion and terms of occupancy, will be forwarded to the Project Manager and the Architect by the Construction Administrator.  A letter will be issued by the Project Manager and Architect to Construction Administrator granting such occupancy and will state the terms and conditions of occupancy.

#### Prior to Agency occupancy, mechanical and electrical systems shall be fully operational.  Required inspections and tests shall have been successfully completed.  Upon occupancy, the Agency will operate and maintain mechanical and electrical systems serving occupied portions of the building.

#### The Architect will prepare a “Certificate of Substantial Completion” for the Work to be occupied prior to Agency occupancy.   Use the “Certificate of Substantial Completion” form as required by the Owner.

Note:  Retain either paragraphs dependent on whether project is  if non threshold limit building or building exceeds threshold limits  Agency will occupy portions of building during construction.  Delete non-applicable paragraph.

#### The Project Manager will request a signed “Certificate of Compliance” from Commissioner of the Department of Public Works, Architect, and Contractor, if required.

OR

#### 5.	The Project Manager will request a signed “Certificate of Compliance” from the Architect, and Contractor, and forward the Certificate to the State Building Inspector a Certificate of Occupancy and obtain the same after his review and approval.

NOTE:  Retain paragraphs below to describe procedures and requirements necessary before Agency occupancy of the project. Modify as necessary.

#### A letter from the Project Manager to the Agency Representative with copy to the General Contractor granting occupancy will state the terms and conditions of occupancy and that fire insurance coverage has been requested, the effective date of which will indicate to the Contractor that he may cancel fire insurance coverage for the project.

#### Upon occupancy, the Agency will assume responsibility for maintenance and custodial service for occupied portions of the building.

#### Work after Agency Occupancy:

##### For all work to complete the occupied building, warranty work, the balancing and commissioning of systems, repair of latent defects and adjustments after occupancy, the contractor is responsible for all costs associated with working in occupied buildings.

## 01019 	CONTRACT CONSIDERATIONS

NOTE:  This Section 01019 "Contact Considerations” includes requirements regarding Cash and Allowances, Unit Prices and submittal of Contractor’s applications for payment under lump sum contracts.  Sample section text is contained to illustrate possible section content.  Revise sample paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

NOTE:  Edit and revise sections below as necessary to suit special project requirements delete if not applicable to Project.

### Allowances:

NOTE:  The use of Allowances is an exception only when the A/E can support their case and get permission from Department of Public Works.  Cash allowances are a method of allocating construction funds to portions of the work, which cannot be specified with specific particularity for competitive bidding at the time of contracting.   Allowances may only be used if permitted by the Project Manager.  If permitted, include the following:

#### The Contractor's costs for unloading and handling, labor, installation costs, storage, insurance, overhead and profit and other expense related to the Allowance item shall be included in the Lump Sum Bid Amount and not in the Allowance unless stated otherwise is the Allowance Schedule of this section.

#### Architect/Engineer:

##### Consult with Contractor for consideration of Products, suppliers and installers.

##### Select Products in consultation with the Project Manager and Agency Representatives and transmit decision to Construction Administrator.

##### Prepare Change Order.

#### Construction Administrator Responsibilities:

##### Consult with Architect/Engineer, Contractor, Project Manager and Agency Representatives for consideration of Products, suppliers and installers.

##### Select Products in consultation with Architect/Engineer, Project Manager and Agency Representatives and transmit decision to Contractor

##### Prepare Change Order.

#### Contractor Responsibilities:

##### Assist Architect/Engineer and Construction Administrator in selection of Products and Suppliers.

##### Obtain proposals from Suppliers and offer recommendations.

##### On notification of selection by Construction Administrator execute purchase agreement with designated supplier.

##### Arrange for and process shop drawings, product data, and samples.  Arrange for delivery.

##### If the actual cost of an Allowance item is more or less than the given amount, the Contract Sum will be adjusted by Change Order.

#### Allowance Schedule:

NOTE:  Show schedule of “Allowances” permitted by Project Manager: Four types of allowances are listed. If permitted, include the following information.  Verify that each referenced section contains a cross-reference to this section and clearly identifies the product to be included under the cash allowance.  Create a sub paragraph below for each cash allowance.  Revise and edit as required for specific project.

##### Section       - “     ”:  Include the Stipulated sum of $       for delivery of      .

##### Section       - “     ”:  Include the Stipulated sum of $       for purchase of      .

##### Section       - “     ”:  Include the Stipulated sum of $       for purchase and delivery of      .

##### Section       - “     ”:  Include the Unit Price of $       for purchase and delivery of      .

### Unit Prices - General:

NOTE:  The definition below assumes a project where the contract documents indicate or provide estimated quantities.  Revise the definition if bidders are required to estimate quantities as well and include them with the bid.

#### Definition - Unit Price: Amount the General Contractor acknowledges in the Bid Proposal Form as a price per unit of measurement for materials or services as described in the Bidding Documents or in the Contract Documents.

#### Procedures:

NOTE:  Retain the requirement below unless the supplementary conditions include similar requirements.

##### Unit Prices included in the Contract Documents are to be used for determining compensation to the Contractor or Owner for changes to the scope of the work indicated in the Contract Documents, and included in the Lump Sum Contract Price.  Special Unit Prices are for items complete, in place, and shall be inclusive of furnishing and installing of all material, labor, trucking, overhead, profit, equipment, hoisting, engineering, scaffolding, power hookups, protection, shop drawings, taxes, permits, appliances, delivery, insurance, supervision, cost of bond, etc. and shall remain in effect until completion of the Contract.

##### Unit Price: Is identified by the Owner as a price per unit of measurement for materials or services added to or deducted from the Contract Sum by appropriate modification, if the estimated quantities of Work required by the Contract Documents are increased or decreased.

##### Increases or Decreases: Should the amount of the Work required be increased or decreased because of changes in the work ordered in writing by the Project Manager, the Undersigned agrees that the following supplemental UNIT PRICES will be decreased 10% for a reduction of work.  Each Unit Price shall include all equipment, tools, labor, permits, fees, etc., incidental to the completion of the work involved.  All items marked with an asterisk (*) in the unit price schedules shall include the completion of the excavation, formation and compaction of sub-grade and the disposal of surplus or unsuitable materials in accordance with the Plans and Specifications or as directed by the Construction Administrator.

NOTE:  Retain the requirement below revise to suite specific project requirements.

#### The Owner reserves the right to reject the Contractor's measurement of work-in-place that involves use of established unit prices, and to have this work measured, at the Owner's expense, by an independent surveyor acceptable to the Contractor.

NOTE:  Retain the requirement below revise to suite specific project requirements.

#### Defect Assessment: Replace the Work, or portions of the Work, not conforming to the specified requirements,  If, in the opinion of the Architect/Engineer it is not practical to remove and replace the work the Architect/Engineer will direct an appropriate remedy or adjust the payment.

NOTE:  Retain the requirement below revise to suite specific project requirements.

#### Unit Price Schedule: A "Unit Price Schedule" is included at the end of this Section.  Specification Sections referenced in the Schedule contain requirements for materials described under each unit price.

NOTE:  This article describes the measurement and payment criteria for applicable to unit price work for earth and rock excavation.  This article should only be used with Work paid by the unit price method.

### Unit Price Schedule - Earth and Rock Excavation: This Section includes administrative and procedural requirements for the following unit prices and provisions are to be included in and become part of this Contract to be used in evaluating additions to or deductions from the work called for in the specifications and/or plans.

#### Unless otherwise specified elsewhere in these documents, Contractors are to assume that all excavation is earth; however, if unspecified rock is encountered, it will be paid for at the given unit prices listed in paragraph “E”.  Rock prices are net in that allowances for reduced quantities of earth are also included in the unit prices.  The prices given include all costs for overhead, profit and rock surveys.

#### Wherever rock to be excavated is encountered, the Contractor shall strip or expose the rock to such an extent that in the Owner’s opinion the necessary measurements can be taken.  The Contractor shall provide the Owner with a survey by a licensed land surveyor indicating top of rock elevations at points of intersection on a rectilinear grid with lines spaced sufficiently close to show accurately the rock surface contours.  At the Owner’s option, an additional survey may be furnished by the Owner from a licensed surveyor.

#### If the conditions of the excavation work indicated are clearly of a special nature, the Contractor may ask the Owner for reconsideration of the established unit prices and if granted, the unit prices will not apply, and prices will be negotiated in accordance with Article 13 “Compensations for Changes in the Work” of the General Conditions.

### Definitions:

NOTE:  The definitions below assume a project where the contract documents indicate or provide estimated quantities and bidders state on the bid form the unit price amounts they propose.  Revise the definition if bidders are required to estimate quantities as well and include them with the bid.

#### “EARTH” - is defined, as excavation shall include removal of all materials other than ‘water’ and ‘rock’.

#### “ROCK” - is defined as a boulder of 1 cubic yard or more in volume (1/2 cubic yard for a boulder in trenches), and rock in definite ledge formation and masonry structures of one cubic yard or more in volume, the removal of which requires the use of mechanical equipment or the use of explosives.  Rock removed by scarification or ripping method is considered as a separate classification under paragraph 4.a.(1).

#### “ORIGINAL GRADE” - is defined as being the grade which exists at the time of Contract Award.

#### “ROUGH GRADE” - is defined as being the completed surface of required excavations greater than 13’ in width.

#### “MASS” - excavation is to be considered as an open area whose minimum horizontal dimensions exceeds 13’.

#### “TRENCH” - is defined as excavation is defined as the removal of material from areas 13 feet or less in its minimal horizontal dimensions and below the elevation of rough grade or original grade, whichever is lower.

### Procedures:

NOTE:  Retain the requirement below unless the supplementary conditions include similar requirements.

#### Rock Excavation In Trenches: Basis For Horizontal Measurement:

##### Horizontal Measurements: Will be taken between the vertical planes as defined below.

##### The Minimum Width Of Trenches In Rock: Will be taken as 3’ 0”.

##### Excavation - For Walls Or Piers With Footings: The measurements will be taken parallel to and one foot outside of the edges of the concrete footings as called for in the plans (i.e. for 4’ 0” footing, rock will be taken as 6’ 0” in width).

##### Excavation For Walls Or Piers Without Footings: The limits of the excavation will be 1’ 6” outside of the line of concrete at bottom as shown or called for in the plans (i.e. for a wall with a bottom thickness of 1’ 0”, the width of the trench will be considered to be 4’ 0”).  (Caissons are excluded from these measurements).

##### Excavation For Pipe Lines: Will be measured at 2’ 0” more than the nominal inside diameter of the pipe but in no case less than 3’ 0” wide.

##### Excavation For Tanks, Vaults, Manholes, Pits, Etc.: Will be measured as 2’ 0” greater in both length and width or diameter than the actual exterior dimensions of the structures and this excavation is considered to be trench only if any measured horizontal dimensions is 13’ or less.

##### No allowance will be made for rock removed beyond the above limits.

#### Rock Excavation In Trenches - Basis for Vertical Measurement:

##### To determine depth of trench, vertical measurements will be taken from original grade or rough grade, (whichever is applicable), to the bottom of required excavation.  These measurements will define the maximum depths for payments.

##### To determine quantity of rock in trench, vertical measurements will be taken from the top of rock as encountered in the trench to 12” below the bottom of required rock excavation.  Any over excavation below the required elevation shall be filled with concrete or other material as specified at no cost to the Owner.

##### No allowance will be made for rock removed beyond the above limits.

#### Earth Excavation In Trenches - Basis Of Measurement: (Horizontal & Vertical): The basis of measurements and allowance limit for earth excavation in trenches is identical to that indicated for rock excavation in trenches, except that there will be no allowance for 12” below the required elevation.  In addition the following will prevail:

##### Maximum allowable widths for earth excavation in trenches without shoring:

| Trench Depth - Classification | Add To Nominal ID Of Pipe Or To Footing Width |
| --- | --- |
|  | 0 ft. - 6 ft. | 3 ft. |
| Over | 6 ft. - 10 ft. | 5 ft. |
| Over | 10 ft. - 15 ft. | 7 ft. |
| Below 15 ft. deep the width of the trench shall be based on the individual case. The final depth of trench will determine the actual width for payment. |

##### If shoring is required the measurement shall be taken between the exterior walls of the shoring not to exceed 4’ plus the I.D. of the pipe (for all depths).

##### To determine quantity of earth in trench, vertical measurements will be taken from the original or rough grade to actual bottom of earth excavation required.

#### Unit Prices - Earth and Rock Excavation (Basis For Payment): Prices include backfill with excavated material if it is suitable.  Prices also include all excavation and disposal of all surplus or unsuitable material.  Where replacement with the excavated material is prohibited or a particular backfill material is specified, the cost of the delivered replacement material in a volume equal to the above excavation pay limits minus the volume of the items installed in the trench shall be paid for a prior negotiated price.  Prices do not include costs of shoring and de-watering but do include sloping for sides of excavation.  Payment and credit amounts shall be determined in the following manner: Widths and depths of trench excavation as indicated.  The total quantity of earth or rock excavation encountered in each depth payment category shall be paid for at its respective unit price as shown below.  For example, in a 15’ trench the first 6’ will be paid for at the 0’ - 6’ price; the next 4’ will be paid for at the over 6’ - 10’ price and the next 5’ will be paid for at the over 10’ - 15’ price.  Thus three different price brackets will prevail.

#### Unit price chart:

NOTE:  Specifications Writers and Project Managers; verify that all unit prices and units listed below are the latest updated information available from DPW.

| a.. | EARTH EXCAVATION - HAND | UNIT | $ ADD | $ DEDUCT |
| --- | --- | --- | --- | --- |
|  | (1) | In Trenches – 0’. - 6’. | C.Y. | 36.00 | 28.80 |
|  | (2) | In Trenches Below 6’ Deep, | Prices Must Be Negotiated Before Work Is Started. |
| b. | EARTH EXCAVATION - MACHINE | UNIT | $ ADD | $ DEDUCT |
|  | (1) | Open Area | All Depths | C.Y. | 7.40 | 5.92 |
|  | (2) | In trenches | 0’ - 4’ deep | C.Y. | 4.25 | 3.40 |
|  |  | Over | 0’ - 10’ deep | C.Y. | 9.00 | 7.20 |
|  |  | Over | 0’ - 15’ deep | C.Y. | 4.75 | 3.80 |
|  |  | Over | 0 - 20’ deep | C.Y. | 5.75 | 4.60 |
| c. | ROCK EXCAVATION | UNIT | $ ADD | $ DEDUCT |
|  | (1) | Open Areas, Rock Removed By Ripping (Any Amount), |  |
|  |  | Net Rock | C.Y. | 9.20 | 7.30 |
|  | (2) | Open Areas, With Explosives - |  |  |  |
|  |  | Net Rock - | Total Quantity Up To 100 | C.Y. | 27.00 | 21.60 |
|  |  |  | Total Quantity Up To 500 | C.Y. | 21.30 | 17.00 |
| d. | ROCK EXCAVATION (cont.) | UNIT | $ ADD | $ DEDUCT |
|  |  |  | Total Quantity Up To 500 or more | C.Y. | 17.00 | 13.60 |
|  | (3) | In Trenches, Boulders, Remove By Machine | C.Y. | 14.00 | 11.20 |
|  | (4) | In Trenches, Ripping Of Rock By Machine | C.Y. | 16.00 | 12.80 |
|  | (5) | In trenches, with explosives |  |  |  |
|  |  | Net Rock | 0’ - 4’ Deep | C.Y. | 20.60 | 16.48 |
|  | (6) | In trenches, with explosives |  |  |  |
|  |  | Net Rock | 0’ - 10’ Deep | C.Y. | 36.75 | 29.40 |
|  | (7 | In trenches, with explosives |  |  |  |
|  |  | Net Rock | 0 - 15’ Deep | C.Y. | 28.60 | 22.88 |
|  | (8) | In trenches, with explosives |  |  |  |
|  |  | Net Rock | Over 15’ - 10’ Deep | C.Y. | 60.00 | 48.00 |
|  | (9) | In trenches, with explosives - |  |
|  |  | Net Rock | 0 - 20’ Deep, | Prices Must Be Negotiated Before Start Of Work. |
|  | (10) | Jack Holes (For Hydraulic Lift/Elevators) | L.F. | 95.00 | 76.00 |
|  | (11) | Open Or Mass Areas - If Explosives Are Prohibited |  |
|  |  | Net Rock | C.Y. | 80.00 | 64.00 |
|  | (12) | Trench Excavation - If Explosives Are Prohibited |  |
|  |  | Net Rock/With Rock Splitters And Jack Hammer or Hoe Ram | C.Y. | 120.00 | 96.00 |

### Unit Price Schedule – Miscellaneous:

Note:  The unit price schedule below includes miscellaneous examples of either owner identified unit prices or unit prices required of the contract and are often encountered in building construction.  The following examples are included to demonstrate possible types.  Revise as necessary to suit project requirements.

#### Unit Price - Miscellaneous:

| a. | MISCELLANEOUS Items | UNIT | $ ADD | $ DEDUCT |
| --- | --- | --- | --- | --- |
|  | a. | *Structural fill |  |  |  |
|  | b. | *Footing forms, contact area |  |  |  |
|  | c. | *Footing concrete, in place |  |  |  |
|  | d. | *Wall forms, contact area |  |  |  |
|  | e. | *Wall concrete, in place |  |  |  |
|  | f. | *Reinforcing steel bars, in place |  |  |  |
|  | g. | *Structural steel, in place |  |  |  |

### Unit Price Schedule - Alterations

Note:  The unit price schedule below includes renovation examples of either owner identified unit prices or unit prices required of the contract and are often encountered in building construction.  The following examples are included to demonstrate possible types.  Revise as necessary to suit project requirements.  Also coordinate with Section 01100 Alteration Projects.  The Architect shall be responsible for completing the unit price schedule for alterations.

#### Unit Price - Alterations:

| a. | ALTERATION ITEMS | UNIT | $ ADD | $ DEDUCT |
| --- | --- | --- | --- | --- |
|  | a. | Roof Blocking |  |  |  |
|  | b. | Roof Planking |  |  |  |
|  | c. | Flashing |  |  |  |
|  | d. | Roof Sheathing |  |  |  |
|  | e. | Roof Flashing |  |  |  |
|  | f. | Structural Deck |  |  |  |
|  | g. | Roof Drain Assemblies |  |  |  |

#### Unit prices shall be negotiated if there is a change in scope of work.

## 01027 APPLICATION FOR PAYMENT

NOTE:  This Section 01027 "Applications for Payment” includes procedural requirements for preparation and submittal of Contractor’s Applications for Payment under lump sum contracts. Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Schedule of Values: Submit the “Schedule of Values” to the Construction Administrator at the earliest possible date but no later than (21) twenty-one Calendar Days after the Contract Start Date.  A separate "Schedule of Values" shall be provided for each Phase of the Project identified in Section 01010 Summary of Work, Work Sequence - Phase(s).

NOTE:  Delete the requirement below if phasing is not required.  For large projects, consider revising the requirement to provide sub-schedules for separate floors or large individual areas.

#### Format and Content:  Use the Project Manual Table of contents as a guide to establish the format for the “Schedule of Values”.   Provide at least one line item for each of the Specification Section on electronic media printout.

#### Identification: Project identification on the Schedule of Values shall include, but not be limited to, the following:

NOTE:  Modify the list below to suit project requirements by adding or deleting items.

##### Owner

##### Project Number

##### Project Name

##### Project Location

##### Contractor's name and address.

#### Arrange the “Schedule of Values” in tabular format as required by the Owner, containing separate columns including, but not limited to, the following Items:

NOTE:  Modify the list below to suit project requirements by adding or deleting items

##### Item Number.

##### Description of Work with Related Specification Section or Division Number.

##### Scheduled Values broken down by description number, type material, units of each material.

##### Name of subcontractor.

##### Name of manufacturer or fabricator.

##### Name of supplier.

##### Retainage.

##### Contract sum in sufficient detail.

#### Percentage of Contract Sum to nearest one-hundredth percent, adjusted to total 100 percent.

#### Provide a breakdown of the Contract Sum in sufficient detail to facilitate continued evaluation of Applications for Payment and progress reports.  Coordinate with the Project Manual table of contents.  Break principal subcontract amounts down into several line items.

#### Round amounts to nearest whole dollar; the total shall equal the Contract Sum.

NOTE:  Retain the requirement below.  Strengthen to protect against undue front-end loading, if necessary. Delete the requirement below if specifications do not include unit-cost allowances.

#### Unit-Cost Allowances:  Show the line-item value of unit-cost allowances, as a product of the unit cost, multiplied by the measured quantity.  Estimate quantities from the best indication in the Contract Documents.

NOTE:  Retain the requirement below.  Modify as required to suit project requirements.

#### General Conditions:  Show line items for indirect costs and margins on actual costs only when such items are listed individually in Applications for Payment.  Each item in the Schedule of Values and Applications for Payment shall be complete.  Include the total cost and proportionate share of general overhead and profit margin for each item.

##### Temporary facilities and other major cost items that are not direct cost of actual work-in-place may be shown either as separate line items in the Schedule of Values or distributed as general overhead expense, at the Contractor's option.

NOTE:  Revise the requirement below as necessary.

### Applications for Payment - General: Each Application for Payment shall be consistent with previous applications and payments as certified by the Architect and Construction Administrator and paid for by the Owner.

#### The initial “Application for Payment”, the “Application for Payment”, at time of “Substantial Completion”, and the final “Application for Payment”, involve additional requirements.

#### Payment-Application Terms:  The Owner will process monthly progress payments.  The Contractor may submit applications for payment on a monthly basis.

#### Payment-Application Forms:  Use the “Application for Payment” form as required by the Owner.  Present the required information on electronic media printout or approved Owner Form, multiple pages should be used if required.

#### For each item, provide a column including but not limited to the following items:

##### Item Number.

##### Description of Work and Related Specification Section or Division.

##### Scheduled Value, break down by units of material and units of labor.

##### Work completed from previous application.

##### Work completed this period.

##### Materials presently stored.

##### Total completed and stored to date of application.

##### Percentage of Completion.

##### Balance to Finish.

##### Retainage

#### Application Preparation:  Complete every entry on the Application form. At the time of  Final Payment only, include an executed Application form by a person authorized to sign legal documents on behalf of the Contractor.  The Construction Administrator will return incomplete Applications without action.

##### Entries shall match data on the “Schedule of Values”.

##### Include amounts of Change Orders issued prior to the last day of the construction period covered by the application.

NOTE:  Revise the number of copies below to suit specific project or DPW requirements.(Standard is indicated)

#### Transmittal: Except for final payment, submit to the Construction Administrator by a method ensuring receipt within forty-eight (48) hours.  One (1) complete, signed and notarized original of each Application for Payment, including lien waivers and similar attachments when required, along with six (6) copies. For Final Payment, nine (9) complete, signed and notarized copies shall be submitted.

##### Transmit each copy with a transmittal form listing attachments and recording appropriate information related to the application, in a manner acceptable to the Architect.

NOTE:  Insert instructions for preparation and submittal of waivers or releases here if not stated in supplementary conditions.

#### Applications for Payment: Administrative actions and submittals, that must precede or coincide with submittal of the first Application for Payment and all subsequent Application for Payments including, but not limited to, the following items:

NOTE:  Revise the list below to suit project requirements.

##### List of subcontractors and suppliers’ name, FEIN/Social Security numbers, and Connecticut Tax Registration Numbers.

##### List of principal suppliers and fabricators.

##### Schedule of Values.

##### Contractor's Construction Schedule (preliminary if not final).

##### Schedule of principal products.

##### Submittal Schedule (preliminary if not final).

##### List of Contractor's staff assignments.

##### List of Contractor's principal consultants.

##### Copies of all applicable permits.

##### Copies of authorizations and licenses from governing authorities for performance of the Work.

##### Proof that as-built documents are updated as required by Section 01700 “Contract Closeout”.

NOTE:  Delete items submitted before executing the contract from those listed below.

##### Initial as-built survey and damage report, if required.

### Application for Payment at Substantial Completion: Following issuance of the Certificate of Substantial Completion submit an Application for Payment form, use the form as required by the Owner.  Present the required information on electronic media printout.

#### This application shall reflect Certificates of Partial Substantial Completion issued previously for Owner occupancy of designated portions of the Work.

#### Administrative actions and submittals that shall precede or coincide with this application include, but are not limited to, the following:

NOTE:  Delete from and add to the following list to suit project requirements.

##### Occupancy permits and similar approvals.

##### Warranties (guarantees) and maintenance agreements.

##### Test/adjust/balance records.

##### Maintenance instructions.

##### Meter readings.

##### Startup performance reports.

##### Changeover information related to Owner's occupancy, use, operation, and maintenance.

##### Final cleaning.

##### Application for reduction of retainage and consent of surety.

##### Advice on shifting insurance coverage.

##### Final progress photographs.

##### List of incomplete Work, recognized as exceptions to Architect's Certificate of Substantial Completion.

### Final Payment Application: Administrative actions and submittals that must precede or coincide with submittal of the final Application for Payment include, but are not limited, to the following:

NOTE:  Delete from and add to the list below to suit project requirements.  Check with Project Manager about the need for additional affidavits and other requirements.  See requirements for Final Acceptance, Final Completion, Final Inspection, and Final Payment, in the General Conditions and Supplementary Conditions.

#### Completion of Project Closeout requirements.

#### Completion of list of items remaining to be completed as indicated on the attachment to the Certificate of Substantial Completion.

#### Ensure that unsettled claims will be settled.

#### Ensure that incomplete Work is not accepted and will be completed without undue delay.

#### Transmittal of required Project construction records to the Owner (including as-built documents Reference Section 01700 “Contract Closeout”.)

#### Certified property survey.

#### Proof that taxes, fees, and similar obligations were paid.

#### Removal of temporary facilities and services.

#### Removal of surplus materials, rubbish, and similar elements.

#### Change of door locks to Owner's access.

#### The requirements of the General Conditions and Supplementary Conditions for Final Acceptance, Final Completion, Final Inspection, and Final Payment.

#### Asbestos, Lead or other hazardous material manifests.

#### Completion of “Building Contractor Reporting Form” as supplied by Department of Public Works, for all Contractors, Subcontractors, Vendors, Suppliers, etc. who work on the Contract.  The form includes the following information:

##### a.	Contractor/Subcontractor name.

##### FEIN/Social Security Numbers

##### Connecticut Tax Registration Numbers

##### Type of work

##### Name of business and address

##### Remittance address.

## 01030	SUPPLEMENTAL BIDS

NOTE:  This Section 01030 "Supplemental Bids ” includes description of Supplemental bids utilized when the Owner and the Architect/Engineer want to competitively bid additional work or bid a different product or system compared to a product or system specified as an integral part of the base project requirements The submitted bid will be expressed ONLY AS A COST INCREASE to the base price. Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply. "Supplemental Bids ”are also listed in the “Bid Proposal Form” in Division 0 Section 00020, Schedule 7.6.1.

NOTE:  ALL SUPPLEMENTAL BIDS MUST BE CROSSED REFERENCED BETWEEN THIS SECTION AND THE SECTION WHERE THE PRODUCT IS SPECIFIED AS CLEARLY SHOWN ON THE DRAWINGS AND IN THE SPECIFICATIONS “USE LIMIT LINES.”  SHOULD A SUPPLEMENTAL BID REQUIRE PRODUCTS NOT COVERED UNDER THE BASE BID THEN A SECTION MUST BE WRITTEN FOR SUCH PRODUCT AND BOUND IN THE PROJECT MANUAL.  ALL SUPPLEMENTAL BIDS ARE TO BE PRIORITIZED BY THE AGENCY AND MUST BE LISTED NUMERICAL ORDER OF PREFERENCE FOR POSSIBLE INCLUSION IN THE WORK.  ALL SUPPLEMENTAL BIDS MUST BE ACCEPTED CUMMULATIVELY IN THE NUMERICAL ORDER LISTED AND NO SUPPLEMENTAL BID CAN BE SKIPPED OR ACCEPTED OUT OF NUMERICAL ORDER.

NOTE:  For all projects with an estimated construction value that equals or exceeds $250,000.00, the Supplemental Bids must be reviewed to define if subcontractors are to be named.  This would be applicable for sub-trades with an estimated value exceeding $25,000.00. coordinate carefully with Division 0, Section 00020, “Bid Proposal Form” for Schedule 7.5.1 “Named Subcontractors”.  AN ADDITIONAL SECTION MAY BE REQUIRED TO BE ADDED TO THE LIST OF NAMED SUBCONTRACTORS.

NOTE:  The definition below is a normal bidding situation with contractors stating supplemental bids amounts requested on the bid form.  It also assumes that the owner will decide to accept or reject supplemental bids before signing the agreement.  It also assumes that the bidding documents stipulate terms under which the owner will accept or reject the supplemental bids

### Definition:  A Supplemental Bid is an amount proposed by bidders and stated on the Bid Proposal Form for certain work defined in the Bidding Documents that may be added to the Base Bid amount if the Owner decides to accept a corresponding change in either the amount of construction to be completed, or in the products, materials, equipment, systems, or installation methods described in the Contract Documents.

#### The cost for each supplemental bid is the net addition to the Contract Sum to incorporate the Supplemental Bid into the Work.  Supplemental Bids are only accepted in the numerical order that they are listed on the Bid Proposal Form and never accepted out of numerical sequence.  No other adjustments are made to the Contract Sum.

### Procedures:

NOTE:  Make certain it is clear on the Bid Form that costs listed for each supplemental bids include costs of related coordination, modification, or adjustment.  If it is not clearly stated, revise below by stating this requirement.

#### Coordination:  Modify or adjust affected adjacent Work as necessary to completely and fully integrate that Work into the Project.

##### Include as part of each Supplemental Bid, miscellaneous devices, accessory objects, and similar items incidental to or required for a complete installation whether or not mentioned as part of the Supplemental Bid.

NOTE:  Retain the requirement below on most projects.  Failure to require notification could create problems later.

#### Execute accepted Supplemental Bids under the same conditions as other Work of this Contract.

#### Schedule:  A "Schedule of Supplemental Bids" is included at the end of this Section.  Specification Sections referenced in the Schedule contain requirements for materials necessary to achieve the Work described under each Supplemental Bid.

### Schedule of Supplemental Bids:

NOTE:  List Supplemental Bids here.  Identify Supplemental Bids in Division 0 in Section 00020 “Bid Proposal Form” (Section 7.6.1) to permit their inclusion in the Proposal.  Supplemental Bids are selected at the Owner's option.  Supplemental Bids will be listed in the Owner-Contractor Agreement  in order of preference and identified by numbers. i.e.. Supplemental Bid 1,2,3...etc.

NOTE:  Below are some examples of supplemental bids.  They demonstrate possible supplemental bid types.  Revise suitable types as necessary to suit project requirements.

NOTE: Supplemental Bid No.1 is an example of a simple straightforward Supplemental Bid that might necessitate additional specification sections to describe requirements adequately.  Delete or edit and revise as require for specific project.  Drawing information for Supplemental Bids should be bubbled or outlined for clarity.

#### 1.	Supplemental Bid No. 1:  ADD the complete Glycol Foil Heat Recovery Loops into the Project as specified in Section 15600.  It is not included in the Base Bid.

NOTE: Supplemental Bid No. 2 is an example of a simple straightforward Supplemental Bid.  Delete or edit and revise as require for specific project.

#### Supplemental Bid No 2:  ADD the complete space improvements of the 4 laboratory quadrants and the support area as shown on       Drawing       for Floor Level       including all related mechanical and electrical systems, casework, finishes, etc. in order to fully complete the floor.  The Base Bid has this area as being left unfinished.

NOTE: Supplemental Bid No. 3 is an example of a cost comparison type Supplemental Bid where one product or construction method is proposed as a substitute for the product or method specified as part of the base bid.  This type might require adding some specification sections to describe requirements adequately.  Delete or edit and revise as require for specific project.

#### Supplemental Bid No 3:  ADD the complete space improvements of the 4 laboratory quadrants and the support area as shown on       Drawing       but for Floor Level       including all related mechanical and electrical systems, casework, finishes, etc. in order to fully complete the floor.  The Base Bid has this area as being fully completed.

## 01035 MODIFICATION PROCEDURES

NOTE:  The Section 01035 "Modification Procedures” includes detailed procedural requirements for considering change orders. Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Summary:	This Section specifies administrative and procedural requirements for handling and processing contract modifications.

### Requests for Information:

#### In the event that the contractor or subcontractor, at any tier, determines that some portion of the drawings, specifications, or other contract documents requires clarification or interpretation by the Architect, the contractor shall submit a “Request for Information” in writing to the Architect via Construction Administrator.  “Requests for Information” may only be submitted by the contractor and shall only be submitted on the “Request for Information” forms as required by the owner. In the “Request for Information”, the contractor shall clearly and concisely set forth the issue for which clarification or interpretation is sought and why a response is needed from the Architect.

##### In the “Request for Information”, the contractor shall set forth an interpretation or understanding of the requirement along with reasons why such an understanding was reached.

##### The owner acknowledges that this is a complex project. Based upon the owner’s past experience with projects of similar complexity, the owner anticipates that there will probably be some “Requests for Information” on this project.

##### The Architect will review all “Requests for Information” to determine whether they are “Requests for Information” within the meaning of this term. If it is determined that the document is not a “Request for Information”, it will be returned to the contractor, unreviewed as to content, for resubmittal on the proper form and in the proper manner.

##### “Requests for Information Response” shall be issued within seven (7) Working Calendar Days of receipt of the request from the contractor unless the owner determines that a longer time is necessary to provide an adequate response. If a longer time is determined necessary by the owner, the owner will, within seven (7) Working Calendar Days of receipt of the request, notify the contractor of the anticipated response time.  If the contractor submits a “Request for Information” on an activity with seven (7) Working Calendar Days or less of float on the current project schedule, the contractor shall not be entitled to any time extension due to the time it takes the Architect to respond to the request provided that the Architect responds within the seven (7) Working Calendar Days set forth above.

##### “Requests for Information Response” from Architect will not change any requirement of the contract documents. In the event the contractor believes that the “Requests for Information Response” will cause a change to the requirements of the contract document, the contractor shall immediately give written notice to the Construction Administrator stating that the contractor beleives the “Requests for Information Response” will result in “Change Order” and the Contractor intends to submit a “Change Order Proposal” request.  Failure to give such written notice immediately shall waive the contractor’s right to seek additional time or cost under the requirement these Requirements.

### Minor Changes in the Work

### The Architect, through the Construction Administrator, will issue supplemental instruction authorizing minor changes in the Work, not involving adjustment to the Contract Sum or Contract time, on the “Supplemental Instructions” form as required by the Owner.

### Proposal Request:

#### Architect/Owner-Initiated Requests For Proposals: The Architect or Owner will issue a detailed description of proposed changes in the Work via the Construction Administrator that will require adjustment to the Contract Sum or Contract Time.  If necessary, the description will include supplemental or revised Drawings and Specifications.  Such requests shall be on a “Proposal Request” form as required by the owner.

#### “Proposal Request” is issued for information only.  Do not consider them as an instruction either to stop work in progress or to execute the proposed change.

NOTE:  Revise the 14-day time period required below if necessary to suit project requirements.

#### Within Fourteen (14) Working Calendar Days of receipt of a “Proposal Request”, submit an “Change Order Proposal” with the required information necessary to execute the change to the Construction Administrator for the Architect’s/Owner's review.

#### Include a list of quantities of products required and unit costs, with the total amount of purchases to be made.  Where requested, furnish survey data to substantiate quantities.

##### Indicate applicable delivery charges, equipment rental, and amounts of trade discounts.

##### Include a statement indicating the effect the proposed change in the Work will have on the Contract Time.

##### The Agency is tax exempt.  All Contractor and Subcontractor services provided under your contract with the State of Connecticut may not be exempt from taxes.  The Department of Revenue Services can guide you as to which services are exempt and which are not.  Please contact the State of Connecticut, Department of Revenue Services at 1-800-382-9463 or 860 541-3280.

##### Dollar values shown on the Schedule of Values shall not be the governing (or deciding) final amounts for change orders involving either additional charges or deletions.

### Change Order Proposal:

#### When either a “Request for Information” from the Contractor or a “Proposal Request” from the Architect or Owner results in conditions that may require modifications to the Contract, the Contractor may propose changes by submitting a request for a “Change Order Proposal” to the Architect via the Construction Administrator on forms as required by the Owner.  These forms shall also include “Change Order Proposal Worksheets” as required by the Owner.

##### Include statements outlining the reasons for the change and the effect of the change on the Work.  Provide a complete description of the proposed change.  Indicate the effect of the proposed change on the Contract Sum and Contract Time.

##### Include a list of quantities of products required and unit costs, with the total amount of purchases to be made.  Where requested, furnish survey data to substantiate quantities as directed by Article 13 “Compensation for Changes in the Work” of the General Conditions of the Contract for Construction.

##### Indicate applicable delivery charges, equipment rental, and amounts of trade discounts.

##### Comply with requirements in Section 01631 “Equals and Substitutions” if the proposed change requires an equal or substitution of one product or system for a product or system specified.

#### The State of Connecticut construction contract has the following tax exemptions:

##### a.	Purchasing of materials which will be physically incorporated and become a permanent part of the project.

##### b.	Tools, supplies and equipment used in fulfilling the construction contract are not exempt.

##### c.	Services that are resold by the contractor are exempt, i.e. if a General Contractor hires a plumber, carpenter or electrician, a resale certificate may be issued to the subcontractor because these services are considered to be integral and inseparable component parts of the building contract

#### 3.	 “Change Order Request” Forms: Use “Change Order Proposal” and “Change Order Proposal Worksheets” forms as required by Owner.

#### 4.	 “Change Order Proposal” cannot be submitted without the Contractor either prior submission of a “Request for Information” from the Contractor or as a response to a “Proposal Request” submitted by the Architect or Owner.

#### 5.	Any “Change Order Request ” submitted without a prior submittal of a “Request for Information” or as a response to a “Proposal Request” will be immediately rejected and returned to the Contractor.

### Construction Change Directive:

#### 1.	“Construction Change Directive”:  When the Owner and the Contractor disagree on the terms of a “Change Order Proposal” resulting from either a “Request for Information” or “Proposal Request”, then the Architect through the Construction Administrator may issue a “Construction Change Directive” on a “Construction Change Directive” as authorized by the Owner on the form required by the Owner.  The “Construction Change Directive” instructs the Contractor to proceed with a change in the Work, for subsequent inclusion in a “Change Order”.

##### a.	The “Construction Change Directive” contains a complete description of the change in the Work.  It also designates the method to be followed to determine change in the Contract Sum or Contract Time.

#### 2.	Documentation:  The Contractor shall maintain detailed records on a time and material basis of work required by the “Construction Change Directive”.

##### a.	After completion of the change, submit an itemized account and supporting data necessary to substantiate cost and time adjustments to the Contract.

##### b.	The final value shall be negotiated based on the supporting data to determine the value of the work.

### Change Order Procedures:

#### 1.	Upon the Owner's approval of a Contractor’s “Change Order Proposal”, the Construction Administrator will issue a “Change Order” for signatures of the Architect, Owner and the Contractor on “Change Order” form as required by the Owner.

## 01040	COORDINATION

NOTE:  This Section 01040 "Coordination” includes requirements for general project coordination procedures, conservation, coordination of drawings, administrative and supervisory personnel, and cleaning and protection.

Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### A.	Construction Administrator:

#### The Construction Administrator is identified in Division 1 Section 01003 “Construction Administrator”.

#### Construction Mobilization:

##### a.	Cooperate with the Construction Administrator in the allocation of mobilization areas of the site, for field offices and sheds, for agency facility access, traffic, and parking facilities.

##### b.	During Construction, coordinate use of site and facilities through the Construction Administrator.

##### c.	Comply with Construction Administrators procedures for intra-project communications; submittals, reports and records, schedules, coordination drawings, and recommendations; and resolution of ambiguities and conflicts.

NOTE:  Responsibility for providing temporary utilities and construction facilities is identified in Section 01010 “Summary of Work”.  Delete or revise and edit paragraphs below as required for specific project.

##### d.	Comply with instructions of the Construction Administrator for use of temporary utilities and construction facilities.

##### e.	Coordinate field engineering layout as specified in Section 01050 “Field Engineering” for work under the instructions of the Construction Administrator.

### B.	Coordinate construction operations included in various Sections of these Specifications to assure efficient and orderly installation of each part of the Work.  Coordinate construction operations included under different Sections that depend on each other for proper installation, connection, and operation.

#### 1.	Schedule construction operations in the sequence required to obtain the best results where installation of one part of the Work depends on installation of other components, before or after its own installation.

#### 2.	Coordinate installation of different components to assure maximum accessibility for required maintenance, service, and repair.

#### 3.	Make provisions to accommodate items scheduled for later installation.

### C.	Where necessary, prepare memoranda for distribution to each party involved, outlining special procedures required for coordination.  Include such items as required notices, reports, and attendance at meetings.

#### 1.	Prepare similar memoranda for the Construction Administrator, Owner and separate contractors where coordination of their work is required.

### D.	Administrative Procedures: Coordinate scheduling and timing of required administrative procedures with other construction activities to avoid conflicts and assure orderly progress of the Work.  Such administrative activities include, but are not limited to, the following:

NOTE:  Insert other administrative activities needed to suit project requirements.

#### Preparation of schedules.

#### Installation and removal of temporary facilities.

#### Delivery and processing of submittals.

#### Progress meetings.

#### Project closeout activities.

### E.	General Coordination Provisions:

#### 1.	Inspection of Conditions:  Require the Installer of each major component to inspect both the substrate and conditions under which Work is to be performed and coordinate such inspections with the Construction Administrator and authorities having jurisdictions.  If unsatisfactory conditions exist notify the Construction Administrator immediately.  Do not proceed until unsatisfactory conditions have been corrected in an acceptable manner.

#### 2.	The Contractor shall coordinate temporary enclosures with required inspections and tests to minimize the necessity of uncovering completed construction for that purpose.

#### Coordination Drawings:

Edit requirements below for specific project Scope & Size.

##### The HVAC Subcontractor will initiate mylar at 1/4" scale drawings done on AutoCAD showing ducts and piping in plan and section.  Sheet metal shop drawings must be approved prior to starting coordination drawings.

##### The Sprinkler Subcontractor will then superimpose his piping layout on the tracing.

##### The Electrical subcontractor will superimpose all the electrical information on the tracing.  Said information to include but not necessary limited to cable trays, equipment, lighting, conduits, bus duct, etc.

##### The sprinkler subcontractor will complete the coordination drawing by drawing his piping (include pitch) on the tracing.

##### The Construction Administrator will review the completed coordination drawing for general compliance and then submit it to the Architect for his review.  All subcontractors shall rework the mylar drawings until all systems are properly coordinated.

#### The Construction Administrator will meet with the Contractor on all major items of coordination.

#### See also General Conditions Article 7 “Cooperation of Trades”.

## 01045	CUTTING AND PATCHING

NOTE:  This Section 01045 "Cutting and Patching” includes requirements for incidental cutting, fitting and patching required to complete the Work or to make its several parts fit together properly.  This section is NOT intended to be as comprehensive as may be required for an extensive alteration or renovation project.  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Openings and chases may not be shown on the Drawings.  It is the responsibility of the Contractor to examine the Architectural, Electrical, Heating, Cooling, Ventilating and Plumbing Drawings and to provide chases, channels or 	openings where needed.

### The Contractor shall install sleeves, inserts and hangers furnished by the trades needing same.

### After installing work into openings, channels and/or chases, the Contractor shall close same. If finishes are to be restored, the new work shall match the original and shall be done by the trade customarily responsible for the particular kind of work.

### Permission shall be obtained from the Construction Administrator before cutting beams, arches, lintels or other structural members.

### Requirements for Structural Work: Do not cut and patch structural elements in a manner that would change their load-carrying capacity or load-deflection ratio.

#### Obtain approval from the Architect/Engineer’s of the cutting and patching proposal before cutting and patching the following structural elements:

NOTE:  Revise the listed examples below to reflect the project's structural elements.

##### Foundation construction.

##### Bearing and retaining walls.

##### Structural concrete.

##### Structural steel.

##### Lintels.

##### Structural decking.

##### Miscellaneous structural metals.

##### Exterior curtain-wall construction.

##### Equipment supports.

##### Piping, ductwork, vessels, and equipment.

##### Structural systems of special construction in Division 13 Sections.

### Do cutting and patching to integrate all elements of the work.  Provide penetrations of existing surfaces.  Provide samples for testing.  Seal penetrations through floors, walls, ceilings and roofs, as applicable; restore or preserve fire-rated and smoke-barrier construction.  Construction and finishes shall match original work.

### The Contractor shall verify dimensions for built-in work and/or work adjoining that of other trades before ordering any material or doing any work.  Discrepancies shall be submitted to the Construction Administrator before proceeding with the work.

### Existing Warranties: Replace, patch, and repair material and surfaces cut or damaged by methods and with materials in such a manner as not to void any warranties required or existing.

### See also General Conditions Article 23 “Cutting, Fitting, Patching and Digging”.

## 01050	FIELD ENGINEERING

NOTE:  The Section 01050 "Field Engineering” includes requirements for contractor provision of survey and field engineering services for a project.”.  If multiple contracts, responsibility for Work of this section should be identified in Section 01010 “Summary of Work”.  Delete them if they do not apply.

### Provide field engineering services to establish and record grades, lines and elevations.

### The Contractor shall retain a Professional Engineer or Land Surveyor registered by the State of Connecticut to lay out the building, underground utility lines and other site work from the horizontal and vertical control information furnished by the Owner and to establish and record the necessary elevations, at no additional cost to the State.

### The Contractor shall forward a letter from his Land Surveyor or Professional Engineer stating that the control information furnished by the Owner, is accurate or shall identify inaccuracies, if they exist. The Contractor shall not take advantage of errors, which may be included in the control information.  Stakes and markings shall be preserved.

## 01095	REFERENCE STANDARDS & DEFINITIONS

NOTE:  This Section 01095 " Reference Standards & Definitions” includes requirements for compliance with reference standards used in the project manual and for requiring copies of standards at site and definitions of terms that are not defined in the general conditions.  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### For products specified by association or trade standards, comply with requirements of the standard, except when more rigid requirements are specified or are required by applicable codes.

### References to standard specifications and codes refer to the editions current at the bid due date. An exception is, buildings exceeding the threshold limit must be in substantial compliance with the requirements of the effective code at the time of  receipt of completed application to the Office of State Building Inspector (OSBI). References include their addenda and errata, if any, and shall be considered a part of these specifications as if they were printed herein in full.

### The manufacturers' standard warranties or guarantees shall apply when their products are used on this project.

### Flame Spread Ratings - all materials that are required of obligated to meet specified standards shall be submitted to the owner for their records as part of the shop drawing submittal process for their construction records.

## 01120	RENOVATION/DEMOLITION PROJECT PROCEDURES

NOTE:  This Section 01120 "Alteration Project Procedures” includes requirements for performing alteration and renovation Work applicable to all sections of involved in the alterations and procedures for salvageable materials.  Coordinate this section with Division 2 “Selective Demolition” or “Minor Demolitions” or any other sections from Divisions 2 through 17 relating to alteration and renovation Work should specifically reflect this Section..  This Section requires close coordination with drawings and should define scope of Work in the fullest possible detail.  General, broad statements in his section may be interpreted to require more Work than intended, adding to the construction costs unnecessarily, and must be carefully to reflect specific project requirements, or delete them if they do not apply.

### A.	Products For Patching And Extending Work:

#### New materials:  As specified in product sections;  match existing Products and Work .for patching and extending Work.

#### Type and Quality of Existing Products:  Determine by inspecting and testing Products where necessary, referring to existing Work as a standard.

### Inspection- General:

#### Verify that demolition is complete and areas are ready for installation of new Work.

#### Beginning of restoration Work means acceptance of existing conditions.

NOTE:  Include the following Sections and paragraphs for all facilities that have Work Involving Lead Containing Material.  Edit and or delete paragraphs as required for specific project.

### Project Procedures for Work Involving Lead Containing Material (LBP):

#### Exposure levels for lead in the construction industry are regulated by 29 CFR 1926.62.  Construction activities disturbing surfaces containing lead-based paint (LBP) which are likely to be employed, such as sanding, grinding, welding, cutting and burning, have been known to expose workers to levels of lead in excess of the Permissible Exposure Limit (PEL). Conduct demolition and removal Work specified in the technical sections of this specification in conformance with these regulations.  In addition, construction debris/waste may be classified as hazardous waste.  Disposal of hazardous waste material shall be in accordance with 40 CFR Parts 260 through 271 and Connecticut Hazardous Waste Management Regulations Section 22a-209-1; 22a-209-8(c); 22a-449(c)-11; and 22a-449(c)-100 through 110.

NOTE:  Include the following paragraph for all facilities in which children under six years old reside.

#### The Contractor's Work shall be based on a child under the age of six (6) in residence; the Work shall also be in accordance with Connecticut Regulations Section 19a-111-1 through 11.

NOTE:  Include the following paragraph for all facilities constructed prior to 1978.

#### This facility was constructed prior to 1978 and is likely to have painted surfaces containing lead-based paint.

NOTE:  DPW Project Managers should make arrangements for lead inspections by submitting requests to the DPW Asbestos Management Unit.  When the facility has been inspected for the presence of lead-based paint, insert the following paragraph.

#### Testing for lead-based paint has been conducted at the facility scheduled for renovation, demolition, reconstruction, alteration, remodeling, or repair.  Results of the LBP testing are for information purposes only. The testing results are in a separate Volume of this Project Manual.   Under no circumstance shall this information be the sole means used by the Contractor for determining the extent of LBP.  The Contractor shall be responsible for verification of all field conditions affecting performance of the Work.

### Project Procedures for Work Involving Asbestos Containing Material (ACM):

#### The Owner is responsible for abating all ACM that is visible and accessible.  This is to be accomplished through a separate project prior to the start of the renovation project.  In demolition projects, every attempt should by the owner to remove all ACM.

NOTE:  An Owner 24 hour response and testing time and (7) seven working Calendar Days abatement time is included in the paragraph below, if different response time is required, edit and insert a reasonable time period into paragraphs.  The State cannot guarantee any time period for inspection, testing and removal (if necessary).  Edit and or delete paragraphs as required for specific project.

#### If the Contractor should encounter any material suspect or known to contain ACM, he should immediately notify the Construction Administrator of same.  It is the State’s responsibility to have the material tested and abated (if necessary).  The Owner will respond within twenty-four (24) hours after receiving the Contractor’s written request to the Construction Administrator for testing the suspect material.  The Owner will abate ACM (if necessary) within a reasonable time period, i.e. with seven (7) Working Calendar Days.

#### Testing for asbestos has been conducted at the facility scheduled for renovation, demolition, reconstruction, alteration, remodeling, or repair.  Results of the asbestos testing are for information purposes only.  The testing results are in a separate Volume of this Project Manual.  Under no circumstance shall this information be the sole means used by the Contractor for determining the extent of asbestos.  The Contractor shall be responsible for verification of all field conditions affecting performance of the Work.

#### See also General Conditions Article 23 “Cutting, Fitting, Patching and Digging”.

### Project Procedures for Work Involving Products Containing Persistent Bioaccumulative Toxic Chemicals” (PBT’s) such as Polychlorinated Biphenols (PCB’s), Di-2-ethylhexyl Phthalate (DEHP), and Mercury:

#### The Contractor is responsible for abating all PCB’s, DEHP, and mercury prior to the start any work involving construction, renovation or demolition (if necessary).

#### Exposure Levels for  Products Containing Persistent Bioaccumulative Toxic Chemicals (PBT’s) such as PCB’s. DEHP, and mercury in the construction industry is regulated by 29CFR1910.1200 and 29CFR1926.28 et. al.  Construction, renovation or demolition activities disturbing Products Containing Persistent Bioaccumulative Toxic Chemicals” (PBT’s) such as PCB’s and DEHP which are likely to be employed.  These materials include but are not limited to fluorescent light fixture & exit sign, ballast’s, high density discharge (HID) lamps , and certain types of construction products containing vinyl, and  mercury containing electrical switches and thermostats.  These activities may expose workers in excess of the respective Permissible Exposure Limit (PEL).  Conduct demolition and removal Work specified in the technical sections of these specifications in conformance with these regulations.  In addition construction debris/waste may be classified as hazardous waste.  Disposal of all hazardous materials shall be in accordance with but not limited to 40CRF Parts 761 Subpart K, 761, and 761.65 and the Connecticut General Hazardous Waste Statute Sec. 22a-454.

#### A Survey for Products Containing Persistent Bioaccumulative Toxic Chemicals (PBT’s) such as PCB’s, DEHP and Mercury has NOT been conducted at the facility.  Examples include but are not limited to fluorescent light fixture & exit sign, ballast’s, high density discharge(HID) lamps , and certain types of construction products containing vinyl, and  mercury containing electrical switches and thermostats.  It is the Contractors responsibility for verification of all material and field conditions prior to construction, renovation, and demolition that may affect the performance of their Work.

NOTE:  Include the following Sections and paragraphs for all facilities in reference to Asbestos Containing Material (ACM) disclosure and removal..

### Preparation:

#### Cut, move, or remove items as are necessary for access to alterations and renovation Work.  Replace and restore at completion.

#### Remove unsuitable material not marked for salvage, such as rotted wood, corroded metals, and deteriorated masonry and concrete.  Replace materials as specified for finished Work.

#### Remove debris and abandoned items from area and from concealed spaces.

#### Prepare surface and remove surface finishes to provide for proper installation of new Work and finishes.

NOTE:  Include salvageable items in the paragraph below if project includes salvageable materials.  Edit and delete salvageable items if none.

#### Close openings in exterior surfaces to protect existing Work and salvage items from weather and extremes of temperature and humidity.  Insulate ductwork and piping to prevent condensation in exposed areas.

### Installation:

#### Coordinate Work of alterations and renovations to expedite completion and if required sequence Work to accommodate Owner occupancy.

NOTE: Subparagraphs may need to reference Section 01045 “Cutting and Patching”.

#### Remove, cut and patch Work in a manner to minimize damage and to provide restoring Products and finishes to original and or specified condition in accordance with Section 01045 “Cutting and Patching”.

#### Refinish visible existing surfaces to remain in renovated rooms and spaces, to specified condition for each material, with neat transition to adjacent finishes in accordance with Section 01045 “Cutting and Patching”.

NOTE:  Edit the following paragraph and delete inapplicable examples.  Closely coordinate with drawings and with individual product specification sections.

#### In addition to specified replacement of equipment and fixtures, restore existing plumbing, heating, ventilation, air conditioning, electrical, systems to full operational condition.

#### Recover and refinish Work that exposes mechanical and electrical Work exposed accidentally during the Work.

#### Install Products as specified in individual sections.

### Transitions:

#### Where new Work abuts or aligns with existing, perform a smooth and even transition.  Patch work to match existing adjacent Work in texture and appearance.

#### When finished surfaces are cut so that a smooth transition with new Work is not possible, terminate existing surface along a straight line at a natural line of division and make recommendation to Architect/Engineer.

### Adjustments:

#### Where removal of partitions or walls result in adjacent spaces becoming one, rework floors, walls, and ceilings to a smooth plane without breaks, steps, or bulkheads.

NOTE:  Edit the following paragraph and insert appropriate dimensions as applicable to project.  Closely coordinate with drawings and with individual product specification sections. (standard is indicated- If a closer tolerance is required modify the standard)

#### Where a change of plane of ¼ inch in 12 inches or more occurs, request recommendation from Architect/Engineer for providing a smooth transition.

#### Trim existing doors as necessary to clear new floor finish.  Refinish trim as required.

#### Fit Work at penetrations of surfaces as specified in Section 01045 “Cutting and Patching”.

### Repair of Damaged Surfaces:

#### Patch or replace portions of existing surfaces that are damaged, lifted, discolored, or showing imperfections.

#### Repair substrate prior to patching finish.

### Finishes:

#### Finish surfaces as specified in individual Product sections.

#### Finish patches to produce uniform finish and texture over entire area.  When finish cannot be matched, refinish entire surface to nearest intersections.

### Cleaning:

#### In addition cleaning specified in Section 01700 “Project Closeout”, clean Agency occupied areas of Work

## 01121	SALVAGEABLE MATERIALS

NOTE:  On alteration, renovation, demolition and replacement Work, the ownership of the salvageable materials should be investigated and a statement as to whose property it becomes should always be included in the Specifications.  Edit, and add or delete from examples of salvageable items listed below.   If the State or an Agency is to salvage any items then include the location where agency will storage is to be provided.

### The Contractor shall be responsible for removing the following salvageable items from premises and transporting said items to       on      , CT     .

Edit the following examples to suit project.

#### Equipment:

#### Windows:

#### Doors:

#### Door Hardware:

#### Fixtures:

#### Art:

NOTE:  Insert the name and location of the agency facility where salvageable are to be stored.  Also insert the name the agency whose personnel responsible for directing contractor where salvageable materials are to be stored.

### The Contractor shall notify the Construction Administrator in writing (7) seven working Calendar Days prior to removing all salvageable items from the existing alteration project location and unloading all salvageable items at      ,      , Connecticut       and store items in the appropriate location as directed by       personnel.

## 01200	PROJECT MEETINGS

NOTE:  This Section 01200 "Project Meetings” specifies administrative and procedural requirements for project meetings, including but not limited to, the following:  Pre-construction conferences, Pre-installation conferences, and Progress meetings .  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### A.	Pre-construction Conference:

#### The Contractor will attend a Pre-construction Conference before starting construction, as scheduled by the Construction Administrator convenient to the Owner, the Construction Administrator, Architect, and Contractor.  This meeting will take place within fourteen (14) Calendar Days after the written Notice to Proceed and before the Contract Start Date.  Hold the conference at the Project Site or another convenient location as directed by the Construction Administrator.  The Construction Administrator shall conduct the Pre-construction Conference to review the Contractor and Subcontractor responsibilities and personnel assignments.

NOTE:  Amplify the paragraph below as necessary to suit project requirements.

#### Attendees:  Authorized representatives of the Construction Administrator, Owner, Architect, and their consultants; the Contractor and its superintendent; major subcontractors; agency; and other concerned parties shall attend the conference.  All participants at the conference shall be familiar with the Project and authorized to conclude matters relating to the Work.

#### Agenda:  Discuss items of significance that could affect progress, including the following:

NOTE:  Add or delete items in example list below as necessary to suit project requirements.

##### Tentative construction schedule.

##### Critical work sequencing.

##### Progress meeting schedule.

##### Designation of responsible personnel.

##### Procedures for processing field decisions and Change Orders.

##### Procedures for processing Applications for Payment.

##### Distribution of Contract Documents.

##### Submittal of Shop Drawings, Product Data, and Samples.

##### Preparation of record documents.

##### Use of the premises.

##### Parking availability.

##### Office, work, and storage areas.

##### Equipment deliveries and priorities.

##### Safety procedures.

##### First aid.

##### Security.

##### Housekeeping.

##### Working hours.

##### Coordination with Audio-Visual and Telecommunications.

### B.	Progress Meetings:

NOTE:  Modify the paragraph below if the project requires progress meetings on a monthly or weekly basis.

#### The Construction Administrator will conduct progress meetings, bi-weekly, at the Project Site or at regular intervals as agreed upon at the Pre-construction Conference.  The Construction Administrator will notify the Owner, the Architect, and the Contractor of the scheduled Progress Meeting dates.  Coordinate dates of Progress Meetings with preparation of Application for Payment requests.

NOTE:  Modify the paragraph below if attendance by other known entities is necessary.

#### Attendees:  In addition to representatives of the Contractor, Construction Administrator, Owner and the Architect, subcontractor, supplier, or other entity concerned with current progress or involved in planning, coordination, or performance of future activities may be requested to attend these meetings on an as needed basis.  All participants at the meeting shall be familiar with the Project and authorized to conclude matters relating to the Work.  The Contractor shall include the site superintendent as a minimum.

NOTE:  Revise the paragraph below to suit project requirements.

#### Agenda: Progress Meetings shall review and correct or approve minutes of the previous Progress Meeting.  Review other items of significance that could affect progress.  Include topics for discussion as appropriate to the status of the Project.

##### Construction Schedule:  Review progress since the last Progress Meeting.  Determine where each activity is in relation to the required Contractor's “Construction Schedule” and whether each activity is on time or ahead or behind Schedule.  Determine how Work that is behind Schedule will be expedited; secure commitments from parties involved to do so.  Discuss whether Schedule revisions are required to insure that current and subsequent activities will be completed within the Contract Time.

##### Review the present and future needs of each entity present

#### Reporting:  The Construction Administrator will distribute minutes of the meeting to each party present, promptly and before the next scheduled meeting, and to parties who should have been present.

#### A schedule of regular Project Meetings will be established at the Pre-construction Conference.

## 01300 SUBMITTALS

NOTE:  This Section 01300 "Submittals” includes administrative and procedural requirements for submittals required for performance of the Work.  Submittals include the examples of the following types, contractor's construction schedule, submittal schedule, daily construction reports, shop drawings, product data, samples, quality assurance submittals, and proposed "equals" or "substitutions".  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### SUMMARY

#### This Section includes administrative and procedural requirements for submittals required for performance of the Work, including but not limited to the following:

NOTE:  Delete items from the example list below that are not appropriate for the project.  Add items to suit project requirements. Note: the outline below relates to the paragraphs and order that follows in this section.

##### Submittal Procedures.

##### Submittal schedule.

##### Daily Construction reports.

##### Shop Drawings.

##### Shop Drawings for Fire Protection Systems.

##### Product Data.

##### Samples.

##### Quality assurance submittals.

##### Architects Action.

##### Submittals shall comply with all requirements in Division 1 Section 01631 “Equals and Substitutions”.

##### Submittals shall comply with all requirements in Division 1 Section 01740 “Warrantees and Bonds”.

##### Submittals shall comply with all requirements in Division 1 Section 01040 “Coordination”.

##### Submittals shall comply with all requirements in Division 1 Section 01730 “Operation & Maintenance Manuals”.

### Administrative Submittals: Refer to other Division 1 Sections and other Contract Documents for requirements for administrative submittals.  Such submittals include, but are not limited to, the following:

NOTE:  Delete items from the example list below that are not appropriate for the project.  Add items to suit project requirements.

#### Permits.

#### Applications for Payment.

#### Performance and payment bonds.

#### Contractor’s construction schedule.

#### Daily construction reports.

#### Construction Photographs.

#### Insurance certificates.

#### List of subcontractors.

#### Subcontractors/Suppliers FEIN #’s and Connecticut tax registration #.

### Related Sections:  The following Sections contain requirements that relate to this Section:

NOTE:  Delete Division Sections from the list below that are not appropriate for the project.  Add Division Sections to suit project requirements.

#### Division 1 Section 01027 "Application for Payment" specifies requirements for submittal of the Schedule of Values.

#### Division 1 Section 01040 "Coordination" specifies requirements governing preparation and submittal of required Coordination Drawings.

#### Division 1 Section 01200 "Project Meetings" specifies requirements for submittal and distribution of meeting and conference minutes.

NOTE:  Retain paragraph below that is the type of schedule used for the project.  Delete the schedule that is not applicable..

#### Division 1 Section 01310 “Construction Schedules”.

OR

#### Division 1 Section 01315 "CPM Schedule" specifies requirements for contractor's schedule submittal.

#### Division 1 Section 01380 "Construction Photographs" specifies requirements for submittal of periodic construction photographs.

#### Division 1 Section 01400 "Quality Control" specifies requirements for submittal of inspection and test reports.

#### Division 1 Section 01631 "Equals and Substitutions" specifies requirements for submittal of requests to use products other than those specified.

#### Division 1 Section 01700 "Contract Closeout" specifies requirements for submittal of Project Record Documents and warranties at project closeout.

#### Division 1 Section  01740 “Warranties and Bonds”.

### DEFINITIONS

#### Coordination Drawings show the relationship and integration of different construction elements that require careful coordination during fabrication or installation to fit in the space provided or to function as intended and as identified in the Specification Division 2 through 16.

#### Preparation of Coordination Drawings is specified in Division 1 Section "Coordination" and may include components previously shown in detail on Shop Drawings or Product Data.

#### Field samples are full-size physical examples erected on-site to illustrate finishes, coatings, or finish materials.  Field samples are used to establish the standard by which the Work will be judged.

#### Mockups are full-size assemblies for review of construction, coordination, testing, or operation; they are not Samples.

### SUBMITTAL PROCEDURES

#### Coordination:  Coordinate preparation and processing of submittals with performance of construction activities.  Transmit each submittal sufficiently in advance of performance of related construction activities to avoid delay.

#### Coordinate each submittal with fabrication, purchasing, testing, delivery, other submittals, and related activities that require sequential activity.

#### Coordinate transmittal of different types of submittals for related elements of the Work so processing will not be delayed by the need to review submittals concurrently for coordination.

##### The Architect reserves the right to withhold action on a submittal requiring coordination with other submittals until all related submittals are received.

##### The Architect reserves the right to reject incomplete submitted packages.

#### Processing:  To avoid the need to delay installation as a result of the time required to process submittals, allow sufficient time for submittal review, including time for resubmittals.

NOTE:  Revise the time  periods of subparagraphs below to suit project requirements.

##### Allow (2) two weeks for initial review.  Allow additional time if the Architect must delay processing to permit coordination with subsequent submittals.

##### If an intermediate submittal is necessary, process the same as the initial submittal.

##### Allow (2) two weeks for reprocessing each submittal.

##### No extension of Contract Time will be authorized because of failure to transmit submittals to the Architect sufficiently in advance of the Work to permit processing.

NOTE:  Revise the submittal formats of subparagraphs below to suit project requirements.

### Submittal Preparation:  Place a permanent label, title block or 8-1/2 inches x 11 inches cover page approved by the Architect, on each submittal for identification.  Indicate the name of the entity that prepared each submittal on the label or title block.

#### The minimum number of copies required for each submittal shall be at a minimum 7 copies or as determine otherwise at the pre-construction conference or by the Construction Administrator.

#### Provide a space approximately 4 inches by 5 inches on the label, beside the title block or on the cover page on Shop Drawings to record the Contractor's review and approval markings and the action taken.

#### Include the following information on the label for processing and recording action taken.

NOTE:  Delete items from the example list below that are not appropriate for the project.  Add items to suit project requirements.

##### Project Name and State of Connecticut Project Number.

##### Date.

##### Name and address of the Architect, Construction Administrator, and Owner Representative.

##### Name and address of the Contractor.

##### Name and address of the subcontractor.

##### Name and address of the supplier.

##### Name of the manufacturer.

##### Number and title of appropriate Specification Section.

##### Drawing number and detail references, as appropriate.

##### Indicate either initial or resubmittal.

##### Indicate deviations from Contract Documents.

##### Indicate if "equal" or "substitution".

NOTE:  Revise the submittal process with copy of the transmittal to Construction Administrator and original to Architect as required.

### Submittal Transmittal:  Package each submittal appropriately for transmittal and handling.  Transmit each submittal from the Contractor to the Architect using a transmittal form.  Copy the Construction Administrator on the transmittal.  The Architect will return all submittals to the Contractor after action is taken with a complete copy of the submittal package and one complete copy of the submittal package.  The Architect will not accept submittals received from sources other than the Contractor.

#### 1.	On the transmittal, record relevant information and requests for data.  On the form, or separate sheet, record deviations from Contract Document requirements, including variations and limitations.  Include Contractor's certification that information complies with Contract Document requirements.

### SUBMITTAL SCHEDULE

NOTE:  Revise the time periods of subparagraph below to suit project requirements.

#### After development and review by the Owner and Architect acceptance of the Contractor's Construction or CPM schedule prepare a complete schedule of submittals.  Submit the schedule to the Construction Administrator within 30 days of Contract Award.

#### Coordinate Submittal Schedule with the list of subcontracts, Schedule of Values, and the list of products as well as the contractor’s Construction or CPM Schedule.

#### Prepare the schedule in chronological order.  Provide the following information:

##### Schedule date for the initial submittal.

##### Related section number.

##### Submittal category (Shop Drawings, Product Data, or Samples).

##### Name of Subcontractor.

##### Description of the part of Work covered.

##### Scheduled date for resubmittal.

##### Scheduled date for the Architect’s final release of approval.

### Distribution:  Following response to the initial submittal, print and distribute copies to the Construction Administrator, Architect, Owner, subcontractors, and other parties required to comply with submittal dates indicated.  Post copies in the Project meeting room and field office.

#### When revisions are made, distribute to the same parties and post in the same locations.  Delete parties from distribution when they have completed their assigned portion of the Work and are no longer involved in construction activities.

### Schedule Updating:  Revise the schedule after each meeting or activity where revisions have been recognized or made.  Issue the updated schedule concurrently with the report of each meeting.

### DAILY CONSTRUCTION REPORTS

#### Prepare a daily construction report recording the following information concerning events at the site, and submit duplicate copies to the Construction Administrator at weekly intervals:

NOTE:  Delete items from the example list below that are not appropriate for the project.  Add items to suit project requirements.

##### List of subcontractors at the site.

##### Approximate count of personnel at the site.

##### High and low temperatures, general weather conditions.

##### Accidents and unusual events.

##### Meetings and significant decisions.

##### Stoppages, delays, shortages, and losses.

##### Meter readings and similar recordings.

##### List of equipment on site and identify if idle or in use.

##### Orders and requests of governing authorities.

##### Change Orders received, start and end dates.

##### Services connected, disconnected.

##### Equipment or system tests and startups.

##### Partial Completion’s, occupancies.

##### Substantial Completion’s authorized.

##### Equals or Substitutions approved or rejected.

### SHOP DRAWINGS

NOTE:  Revise the submittal formats of subparagraphs below to suit project requirements.

#### Submit newly prepared information drawn accurately to scale.  Highlight, encircle, or otherwise indicate deviations from the Contract Documents.  Do not reproduce Contract Documents or copy standard information as the basis of Shop Drawings.  Standard information prepared without specific reference to the Project is not a Shop Drawing.

#### Shop Drawings include fabrication and installation Drawings, setting diagrams, schedules, patterns, templates and similar Drawings.  Include the following information:

##### Dimensions.

##### Identification of products and materials included by sheet and detail number.

##### Compliance with specified standards.

##### Notation of coordination requirements.

##### Notation of dimensions established by field measurement.

##### Sheet Size:  Except for templates, patterns and similar full-size Drawings, submit Shop Drawings on sheets at least 8-1/2 by 11 inches but no larger than 36 by 48 inches.

##### Submit one (1) reproducible media and seven (7) prints as directed by the Construction Administrator.  The Contractor's submittal shall identify the specification section and/or drawing number applicable to the submittal.

##### Details shall be large scale and/or full size.

#### The Contractor shall review the Shop Drawings, stamp with this approval, and submit them with reasonable promptness and in orderly sequence so as to cause no delay in his Workor in the Workof any subcontractor.  Shop Drawings shall be properly identified as specified for item, material, workmanship, and project number.  At the submission, the Contractor shall inform the Architect, in writing of any deviation in the shop drawings from the requirements of the Contract Documents.

#### The Architect will review and comment on shop drawings with reasonable promptness so as to cause no delay, but only for conformance with the design concept of the project and with the information given in the Contract Documents.  Refer to Article 5 of General Conditions.  Shop Drawings received by the Architect that indicate insufficient study of drawings and specifications, illegible portions or gross errors, will be rejected outright.  Such rejections shall not constitute an acceptable reason for granting the Contractor additional time to perform the work.

#### The Contractor shall make any corrections required by the Architect and shall resubmit the required number of corrected copies of shop drawings until fully reviewed.

#### Upon final review submit four (4) additional prints, same as submitted, to the Construction Administrator for his use.

#### The Architect's review and comments on shop drawings shall not relieve the Contractor of responsibility for any deviation from the requirements of the Contract Documents.

#### Only final reviewed shop drawings are to be used on the project site.

#### The Work installed shall be reviewed in accordance with the shop drawings and the drawings and specifications.  Final Review of the shop drawings by the Architect shall constitute acceptance by the State and the Architect of a variation or departure that is clearly identified.  Final reviewed shop drawings shall not replace or be used as a vehicle to issue or incorporate change orders.

### SHOP DRAWING FOR FIRE PROTECTION SYSTEMS

#### Shop drawings for fire protection systems shall comply with all of the requirements in the section above “Shop Drawings” In addition Sprinkler system shop drawings and hydraulic calculations must be stamped by a professional engineer licensed in the state of Connecticut and must include the DPW project number.  Two (2) sets of information [as noted in Division 1 “Submittals” Section 01300] shall be submitted to the State's Insurance Carrier (SIC), and one (1) set shall be submitted to a) the State Fire Marshals (SFM) office for projects exceeding statutory threshold limit or b) to DPW Code Unit for those projects which do not exceed statutory threshold limit.

STATE INSURANCE CARRIER  (SIC):

FM Global

Factory Mutual Insurance Company

P.O. Box 9102 500 River Ridge Drive

Norwood, MA 02062

Tel: (781) 440-8000 or FAX (781) 440-8742

Contact: Costa Terzides (781) 440-8204 or Jeannette Dantona (781) 440-8245

| Exceeds Threshold |  | Does not exceed threshold |
| --- | --- | --- |
| STATE FIRE MARSHALS (SFM): |  | DPW Codes Unit |
| Deputy State Fire Marshal |  | State Office Building - DPW |
| 1111 Country Club Road, PO Box 2794 |  | 165 Capitol Avenue Room 280 |
| Middletown, CT 06457 |  | Hartford, CT 06106 |
| Tel: (860) 685-8350 |  | Ira Henowitz (860) 713 5708 or |
|  |  | Lisa Humble (860) 713-5729 |

Before the shop drawings are submitted to SIC or Code (either SFM or DPW), the A/E and/or the A/E fire protection consultant must review the sprinkler design for compliance with the code and DPW requirements.  SIC review comments will be addressed to the DPW Chief Engineer.  The DPW Chief Engineer shall confirm to the A/E any changes required by SIC/SFM.  The A/E is responsible for changes that result from the SIC and/or Code (SFM or DPW) required during construction.

The State Insurance Carrier (SIC) requires two- (2) weeks prior notice of a sprinkler system acceptance test.

### PRODUCT DATA

#### Collect Product Data into a single submittal for each element of construction or system.  Product Data includes printed information, schedules, such as manufacturer's installation instructions, catalog cuts, standard color charts, roughing-in diagrams and templates, standard wiring diagrams, and performance curves.

#### Mark each copy to show applicable choices and options.  Where printed Product Data includes information on several products that are not required, mark copies to indicate the applicable information.  Include the following information:

Revise the submittal formats of subparagraphs below to suit project requirements.

##### Manufacturer's printed recommendations.

##### Compliance with trade association standards.

##### Compliance with recognized testing agency standards.

##### Application of testing agency labels and seals.

##### Notation of dimensions verified by field measurement.

##### Notation of coordination requirements.

#### Do not submit Product Data until compliance with requirements of the Contract Documents has been confirmed.

#### Preliminary Submittal:  Submit a preliminary single copy of Product Data where selection of options is required.

#### Submittals:  Submit 7 copies of each required submittal; submit 5 copies where required for maintenance manuals.  The Architect will retain one and will return the other marked with action taken and corrections or modifications required.

##### a.	Unless noncompliance with Contract Document provisions is observed, the submittal may serve as the final submittal.

#### Distribution:  Furnish copies of final submittal to installers, subcontractors, suppliers, manufacturers, fabricators, and others required for performance of construction activities.  Show distribution on transmittal forms.

##### Do not proceed with installation until a copy of Product Data is in the Installer's possession.

##### Do not permit use of unmarked copies of Product Data in connection with construction.

NOTE:  Projects requiring sample full-scale mock-ups, the Architect shall identify below and with technical specifications.

### SAMPLES

#### Submit full-size, fully fabricated Samples cured and finished as specified and physically identical with the material or product proposed.  Samples include partial sections of manufactured or fabricated components, cuts or containers of materials, color range sets, and swatches showing color, texture, and pattern.

#### Store, mount or display Samples on site in the manner to facilitate review of qualities indicated.  Prepare Samples to match the Architect's sample.  Include the following:

##### Specification Section number and reference.

##### Generic description of the Sample.

##### Sample source.

##### Product name or name of the manufacturer.

##### Compliance with recognized standards.

##### Availability and delivery time.

#### Submit Samples for review of size, kind, color, pattern, and texture.  Submit Samples for a final check of these characteristics with other elements and a comparison of these characteristics between the final submittal and the actual component as delivered and installed.

##### Where variation in color, pattern, texture, or other characteristic is inherent in the material or product represented, submit at least (3) three multiple units that show approximate limits of the variations.

##### Refer to other Specification Sections for requirements for Samples that illustrate workmanship, fabrication techniques, details of assembly, connections, operation, and similar construction characteristics.

##### Refer to other Sections for Samples to be returned to the Contractor for incorporation in the Work.  Such Samples must be undamaged at time of use.  On the transmittal, indicate special requests regarding disposition of Sample submittals.

##### Samples not incorporated into the Work, or otherwise designated as the Owner's property, are the property of the Contractor and shall be removed from the site prior to Substantial Completion.

#### Preliminary Submittals:  Submit a full set of choices where Samples are submitted for selection of color, pattern, texture, or similar characteristics from a range of standard choices, unless otherwise noted in specification section..

##### a.	The Architect will review and return preliminary submittals with the Architects notation, indicating selection and other action.

#### Submittals:  Except for Samples illustrating assembly details, workmanship, fabrication techniques, connections, operation, and similar characteristics, submit (3) sets.  The Architect will return one set marked with the action taken.

#### Maintain sets of Samples, as returned, at the Project Site, for quality comparisons throughout the course of construction.

##### Unless noncompliance with Contract Document provisions is observed, the submittal may serve as the final submittal.

##### Sample sets may be used to obtain final acceptance of the construction associated with each set.

#### Distribution of Samples:  Prepare and distribute additional sets to subcontractors, manufacturers, fabricators, suppliers, installers, and others as required for performance of the Work.  Show distribution on transmittal forms.

##### a.	Field samples are full-size examples erected on-site to illustrate finishes, coatings, or finish materials and to establish the Project standard.

###### Comply with submittal requirements to the fullest extent possible.  Process transmittal forms to provide a record of activity.

### QUALITY ASSURANCE SUBMITTALS

#### Submit quality-control submittals, including design data, certifications, manufacturer's instructions, manufacturer's field reports, and other quality-control submittals as required under other Sections of the Specifications.

#### Certifications:  Where other Sections of the Specifications require certification that a product, material, or installation complies with specified requirements, submit a notarized certification from the manufacturer certifying compliance with specified requirements.

##### Signature:  Certification shall be signed by an officer of the manufacturer or other individual authorized to sign documents on behalf of the company.

#### Inspection and Test Reports:  Requirements for submittal of inspection and test reports from independent testing agencies are specified in Division 1 Section "Quality Control."

NOTE:  Architect to edit the action language to meet the intent of the language examples listed.

### ARCHITECT'S ACTION

#### Except for submittals for the record or information, where action and return is required, the Architect will review each submittal, mark to indicate action taken, and return promptly.

##### Compliance with specified characteristics is the Contractor's responsibility.

#### Action Stamp:  The Architect will stamp each submittal with a uniform, action stamp.  The Architect will mark the stamp appropriately to indicate the action taken, as follows:

##### Final Unrestricted Release:  When the Architect marks a submittal "Approved for fabrication," the Work covered by the submittal may proceed provided it complies with requirements of the Contract Documents.  Final payment depends on that compliance.

##### Final-But-Restricted Release:  When the Architect marks a submittal "Incorporate Notations," the Work covered by the submittal may proceed provided it complies with notations or corrections on the submittal and requirements of the Contract Documents.  Submit corrected copies for record.  Final payment depends on that compliance.

##### Returned for Resubmittal:  When the Architect marks a submittal "Rejected, or Revise and Resubmit," do not proceed with Work covered by the submittal, including purchasing, fabrication, delivery, or other activity.  Revise or prepare a new submittal according to the notations; resubmit without delay.  Repeat if necessary to obtain different action mark.

###### Do not use, or allow others to use, submittals marked "Rejected, or Revise and Resubmit" at the Project Site or elsewhere where Work is in progress.

###### Other Action:  Where a submittal is for information or record purposes or special processing or other activity, the Architect will return the submittal marked "Action Not Required."

##### Unsolicited Submittals:  The Architect will discard unsolicited submittals without action.

## 01310	CONSTRUCTION SCHEDULE

NOTE:  This Section 01310 "Construction Schedules ” includes requirements administrative and procedural requirements for preparation, submittal, and updating of the Contractor’s construction schedules and reporting progress of the Work.  It is appropriate for small single contract work.  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.  USE THIS SECTION WHEN THE PROJECT TO BE ADMINISTRATED HAS A CONSTRUCTION COST ESTIMATE UNDER $5,000,000

### Definitions:

#### Construction Schedule: A method of planning and scheduling a construction project utilizing a horizontal bar chart with a separate bar for each major portion of the Work or operation to make the schedule an effective tool for planning and monitoring the progress of the work.

### Quality Assurance:  The Contractor's Consultant: Retain a consultant to provide planning, evaluating, and reporting by CPM scheduling.

NOTE:  Retain paragraph below where the Work will be conducted under a single prime contract.  Delete for multiple prime contracts.  Revise if the owner wants to retain an independent consultant.

NOTE:  Delete subparagraph below if bidders are not qualified construction scheduling operators or would not be acceptable as operators if qualified.  Delete if the Owner Representative wants contractor to retain an independent consultant.  Review these options with the Owner Representative.  Independent consultants should be impartial in the case of separate prime contractors or if small uncomplicated project.

#### In-house Option: The Owner may waive the requirement to retain a consultant if the Contractor can demonstrate that:

##### The Contractor has the computer equipment required to produce construction schedules.

##### The Contractor employs skilled personnel with experience in construction scheduling and reporting techniques.

NOTE: Insert a specific computer program and hardware configuration if the Microsoft Project program is unacceptable.

#### Program:  Use “Microsoft Project”, latest version.

NOTE:  Manual referenced in subparagraph below contains basic recommendations for construction scheduling procedures and methods.

#### Standards:  Comply with procedures contained in AGC's "Construction Planning & Scheduling."

### Construction Schedule Format:

#### Format:  Utilize a horizontal bar chart (gantt) with a separate bar for each major portion of the Work or operation, identifying first work day of each week.

NOTE: Insert a specific computer program and hardware configuration of and resource loaded Microsoft Project, latest version of the program. Edit scheduling software if this program is too sophisticated for the specific project.

#### Program:  Use Microsoft Project, latest version.

NOTE: Edit Sequence of listings in paragraph below as required for project.

#### Sequence of Listings:  Utilize the Table of Contents of this Project Manual and the chronological order of the start of each item of work.

#### Scale and Spacing:  Provide space for notations and revisions.

NOTE: Edit sheet size  in paragraph below as required for project.

#### Sheet Size:  To be coordinated with Construction Administrator.

### Content:

NOTE:  Edit and revise paragraphs below to suit project.

#### Show complete sequence of construction by activity, with dates beginning and completion of each element of construction.

#### Identify each item by specification section number.

#### Identify work of separate phases other and other logically grouped activities.

#### Show accumulated percentages of completion of each item, and total percentage of Work completed, as of the first day of each month.

#### Provide separate schedule of submittal dates for shop drawings, product data, and samples, Owner/Agency furnished products and any products identified as under Allowances, and dates reviewed submittals will be required from Architect/Engineer.  Indicate decision dates for selection of finishes.

#### Indicate delivery dates for Owner/Agency furnished products and any products identified as under Allowances.

#### Coordinate content with Schedule of Values specified in Section 01027 “Application for Payment”.

#### Indicate critical path with original baseline indicated.

### Submittals And Revisions To Schedules:

#### Indicate progress of each activity to date of submittal, and projected completion date of each activity.

#### Identify activities modified since previous submittal, major changes in scope, and other identifiable changes.

#### Provide narrative report to define problem areas, anticipated delays, and impact on Schedule.  Report corrective action taken, or proposed, and its effect.

NOTE:  Projects requiring a Construction Schedule should begin with a preliminary bar-chart (gantt) schedule of the type described below.  Revise times given in paragraph below to suit project.

#### An initial bar graph (gantt) schedule is to be prepared by the General Contractor and submitted to the Construction Administrator within seven (7) Working calendar days of award of contract.  This schedule is to cover all items of work from the start of the project up to the completion of the project.  After review, resubmit required revised data within five (5) Working calendar days.  This schedule must be revised monthly and when the actual schedule of significant items varies more than seven (7) Calendar days from the proposed schedule. The critical path with baseline must be indicated.

#### Submit revised Construction Schedules each Application for Payment.

#### Submit four (4) copies of the Construction Schedule to the Construction Administrator..

### Distribution:

#### Distribute copies of the Construction Schedules to Construction Administrator, Architect, Owner, Subcontractors, suppliers, and other concerned parties.

#### Instruct recipients to promptly report, in writing, problem anticipated by projections indicated in schedules.

## 01380	CONSTRUCTION PHOTOGRAPHS

NOTE:  This Section 01380 “Construction Photographs” requirements include administrative and procedural requirements for construction photographs of the Work.  This section does not apply to all projects; determine need with Project Manager including number of photos.

### On the date the work is begun and every thirty (30) days thereafter (typically at the end of the month- until the work is at least 95 percent complete), the Contractor shall have photographs of the construction taken by a professional photographer or an individual approved by the Owner.

NOTE:  Revise paragraph below to satisfy office policy and project requirements.  Change number of photos required complying with distribution requirements. A standard 24 is shown, may modify to 12 or 36.

### Photographs: Provide a digital camera to take (24) or more photos each time. Deliver 1 sets of photo files on CD-ROM and one set of prints to the Construction Administrator for the department. Label each CD-ROM with project name and the date the photographs were taken. With each submittal provide an index sheet of digital photos and where the photos were taken.

### As photographs are a record of the work progress, they shall be taken each month, whether or not they show work done during the preceding month.  Deliver digital photos to the Construction Administrator within 10 days of their taking.

## 01400	QUALITY CONTROL

NOTE:  This Section 01400 "Quality Control” includes requirements for quality assurance and inspecting and testing laboratory services.  It is appropriate for complex single contract work.   Edit paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Contractor Responsibilities: Unless otherwise indicated as the responsibility of another identified entity, the Owner, through the Construction Administrator, shall provide Fire Alarm Acceptance testing, inspections, tests, and other quality-control services specified elsewhere in the Contract Documents and required by authorities having jurisdiction.  All tests required by the individual specification sections are required to be scheduled and notification given to the Construction Administrator twenty-four (24), forty-eight (48) hours in advance to the test/inspection as applicable.  Costs for these services are not included in the Contract Sum.

#### Where individual Sections specifically indicate that certain inspections, tests, and other quality-control services are the Contractor's responsibility, the Contractor shall employ and pay a qualified independent testing agency to perform quality-control services.  Costs for these services are included in the Contract Sum.

#### Where individual Sections specifically indicate that certain inspections, tests, and other quality-control services are the Owner's responsibility, the Owner will employ and pay a qualified independent testing agency to perform those services.

##### Such services include Special Inspections as required by the latest adoption of the “Connecticut State building Code”.

##### Where the Owner has engaged a testing agency for testing and inspecting part of the Work, and the Contractor is also required to engage an entity for the same or related element, the Contractor shall not employ the entity engaged by the Owner.  The Owner will engage the services of a qualified Special Inspector for this project.  The Special Inspector, as a representative of the Owner, shall document and confirm compliance with the provisions of the Connecticut State Building Code for Special Inspections.

##### Materials and assemblers for this project will be tested and construction operations inspected as the work progresses.  Failure to detect any defective work or material shall not in any way prevent later rejection when such defect is discovered nor shall it obligate the State for final acceptance.

##### The Owner use of testing and inspection services shall in no way relieve the contractor of the responsibility to furnish materials and finished construction in full compliance with the Contract Documents and the Connecticut State Building Codes.

### Retesting:  The Contractor is responsible for retesting where results of inspections, tests, or other quality-control services prove unsatisfactory and indicate noncompliance with Contract Document requirements, regardless of whether the original test was Contractor's responsibility.

#### The cost of retesting construction, revised or replaced by the Contractor, is the Contractor's responsibility where required tests performed on original construction indicated noncompliance with Contract Document requirements.

#### The Owner will issue a credit change order to cover all costs incurred related to all re-tests/re-inspection due to non-compliance to the contract documents, including but not limited to the Owners costs and the Consultants costs.

### Associated Services: Cooperate with agencies performing required inspections, tests, and similar services, and provide reasonable auxiliary services as requested.  Notify the agency sufficiently in advance of operations to permit assignment of personnel.  Auxiliary services required include, but are not limited to, the following:

#### Provide access to the Work.

#### Furnish incidental labor and facilities necessary to facilitate inspections and tests.

#### Take adequate quantities of representative samples of materials that require testing or assist the agency in taking samples.

#### Provide facilities for storage and curing of test samples.

#### Deliver samples to testing laboratories.

#### Provide an approved design mix proposed for use for material mixes that require control by the testing agency.

#### Provide security and protection of samples and test equipment at the Project Site.

NOTE:  Retain the following paragraph on duties of the testing agency when contractor employs the agency.

### Duties of the Testing Agency:  The independent testing agency engaged to perform inspections, sampling, and testing of materials and construction specified in individual Sections shall cooperate with the Construction Administrator, Architect and the Contractor in performance of the testing agency's duties.  The testing agency shall provide qualified personnel to perform required inspections and tests.

#### The testing agency shall notify the Construction Administrator and the Contractor promptly of irregularities or deficiencies observed in the Work during performance of its services.

#### The testing agency is not authorized to release, revoke, alter, or enlarge requirements of the Contract Documents or approve or accept any portion of the Work.

#### The testing agency shall not perform any duties of the Contractor.

NOTE:  List any special requirements regarding testing.

### Owner will pay for the services of an independent testing agency laboratory to perform inspections, tests and other services required by the Specifications except as noted below, listed for which the Owner will issue a deduct change order to cover the cost associated with these tests:

### When the Contractor notifies the Construction Administrator and/or Testing Agency less than twenty-four (24) hours before the expected time of testing.

### When the Contractor requires testing for his own convenience.

### When the Contractor schedules a test and is not ready for the required test.

### Reports of test that are part of the submittal requirements which indicate compliance or non-compliance with the specified standard.

### See also General Conditions Article 16 “Inspections and Tests”.

NOTE:  Retain the following paragraph on projects that do not exceed the threshold limitations and include either new or upgraded protective service signaling systems.  The Architect must include the required Department of Public Works Testing procedures in the appropriate specification section.

### Fire Alarm/Acceptance Testing Procedures:

#### For buildings exceeding the threshold limit, the fire alarm testing shall be as the authority having jurisdiction shall dictate. This will be as determined by the State Fire Marshals Office.

#### For buildings that do not exceed the threshold limit, the fire alarm testing shall be as the authority having jurisdiction shall dictate. This will be determined by the Department of Public Works requirements as set below:

#### Protective Signaling Systems:

#### All protective signaling systems shall meet with acceptance testing requirements of the applicable standards listed in Section 7-6.1.4, NFPA 101/1997 and NFPA 13/19996.

#### Prior Test Notification:

#### At least 5 working days prior to testing, the Fire Alarm Contractor shall notify (in writing) the following people of the proposed date the acceptance tests are to be performed (Also, see Part 2 of Certificate of Compliance).

#### Department of Public Works Team Representative

#### General Contractor

#### Engineer of Record

#### Equipment Supplier Representative

#### Sprinkler Contractor

#### Certificates of Compliance

###### A Fire Alarm System Inspection and Testing Certification and Description form shall be prepared for each system (See NFPA 72/1999 Chapter 7 and Figure 7-5.2.2).

###### Parts 1 and 3 through 9, shall be completed after the system is installed and the installation of the wiring has been checked.  Every alarm device must also be pre-tested to ensure proper operation and correct annunciation at each remote annunciator and control panel.  Part 1 of the form (Certification of System Installation) shall be signed by the fire alarm contractor. The signed and completed preliminary copies of the Certification form shall be forwarded to all parties along with the Prior Test Notification.

###### Part 2, of each applicable form, shall be completed after the operational tests have been completed.

###### After the completion of the operational acceptance tests and sign-off of test witness (with stipulations noted), final copies of the Certificates shall be forwarded to the Department of Public Works Representatives.

#### Tests:

###### All tests shall be conducted in accordance with the Manufacturers Testing Recommendations.

###### All testing equipment, apparatus (i.e. sound level decibel meter, 2-way radio communication, test devices, ladders, tools, lighting, etc.) and personnel shall be supplied by the Fire Alarm Contractor and Sprinkler Contractor.

#### System Documentation:

#### Every system shall include the following documentation, which shall be delivered to the Department of Public Works Representatives upon final acceptance of the system. An owner's manual or manufacturer's installation instructions covering all system equipment, including the following:

- A detailed narrative description of the system inputs, evacuation signaling, ancillary functions, annunciation, intended sequence of operations, expansion capability, application considerations, and limitations.

- Operators instructions for basic systems operations including alarm acknowledgment, system reset, interpreting system output (LED's CRT display, and printout), operation of manual evacuation signaling and ancillary function controls, changing printer paper, etc.

- A detailed description of routine maintenance and testing as required and recommended and as would be provided under a maintenance contract, including testing and maintenance instructions for each type of device installed. This information should include:

#### a. A listing of individual system components that require periodic testing and maintenance.

#### b. Step by step instructions detailing the requisite testing and maintenance procedures and the intervals at which those procedures should be performed.

#### c. A schedule that correlates the testing and maintenance procedures required by paragraph (2) above and with the listing required by paragraph (1) above.

- Detailed troubleshooting instructions for each type of trouble condition recognized by the system, including opens, grounds, parity errors, "loop failures," etc. These instructions should include a list of all trouble signals, and step by step instructions describing how to isolate those problems and correct them (or call for service as appropriate).

- A service directory, including a list of names and telephone numbers for those who should be called to service on the system.

#### As-Built Drawings:

#### The Contractor will produce two sets of as-built drawings and specifications for the fire alarm system, indicating the location (and programmed address, if applicable) of all devices and appliances, the wiring sequences, wiring methods, connection of the components, and sequence of operation of the protective signaling system as installed, shall be given to DPW representatives. This shall be in Accordance with NFPA 72. Refer also to Section 01700 “Contract Closeout”.

### Submittals:

#### Unless the Contractor is responsible for this service, the independent testing agency shall submit a certified written report, in duplicate, of each inspection, test, or similar service to the Construction Administrator.  If the Contractor is responsible for the service, submit a certified written report, in duplicate, of each inspection, test, or similar service through the Contractor.

#### Submit additional copies of each written report directly to the governing authority, when the authority so directs.

#### Report Data: Written reports of each inspection, test, or similar service include, but are not limited to, the following:

##### Date of issue.

##### Project title and number.

##### Name, address, and telephone number of testing agency.

##### Dates and locations of samples and tests or inspections.

##### Names of individuals making the inspection or test.

##### Designation of the Work and test method.

##### Identification of product and Specification Section.

##### Complete inspection or test data.

##### Test results and an interpretation of test results.

##### Ambient conditions at the time of sample taking and testing.

##### Comments or professional opinion on whether inspected or tested Work complies with Contract Document requirements.

##### Name and signature of laboratory inspector.

##### Recommendations on re-testing.

### Quality Assurance:

#### Qualifications for Service Agencies: Engage inspection and testing service agencies, including independent testing laboratories, that are pre-qualified as complying with the National Voluntary Laboratory Accreditation Program and that specialize in the types of inspections and tests to be performed.

##### Each independent inspection and testing agency engaged on the Project shall be authorized by authorities having jurisdiction to operate in the state where the Project is located.

### Repair and Protection:

#### General:  Upon completion of inspection, testing, sample taking and similar services, repair damaged construction and restore substrates and finishes.  Comply with Contract Document requirements for Division 1 Section "Cutting and Patching."

#### Protect constructions exposed by or for quality-control service activities, and protect repaired construction.

#### Repair and protection is Contractor's responsibility, regardless of the assignment of responsibility for inspection, testing, or similar services.

## 01505	TEMPORARY ELECTRICITY AND LIGHTING

NOTE:  Architect, pay close attention to coordinate these needs with the Department of Public Works and Agency.  Revise as necessary.

### Power and lighting may be taken from the power company's nearest pole with temporary poles, if needed, to extend the line to project.  If permanent power lines have been installed before beginning project, then temporary lines can be brought in from the last pole.

### Provide service required for construction with branch wiring and distribution boxes located to provide power and lighting by construction-type extension cords. Meter shall be provided and installed by the Contractor.

### All costs of temporary power and light shall be paid  by the Contractor.

OR

If work involves an existing facility, the following may be used if approved by the Agency.

If item below is used then delete Items above.

### Connect to existing service, provide branch wiring and distribution boxes located to provide power and lighting by construction-grade extension cords.  Owner will pay cost of energy used.  Take measures to conserve energy.  Provide lighting for construction operations.  At the termination of construction, return the facilities to their original condition.

## 01510	TEMPORARY HEATING, COOLING AND VENTILATING AND LIGHTING

### Provide temporary heat during construction for interior areas included in the Contract to counteract low temperatures or excessive dampness and, in any event, between October 15th and April 15th.  Maintain during said period or periods until final completion of the Contract, unless otherwise approved by the Department of Public Works in writing.  Windows, doors, ventilators and similar openings shall be temporarily closed.  Provide heat and ventilation to maintain specified conditions for construction operations and to protect materials and finishes from damage by temperature or humidity. The permanent heating system is not to be used for temporary heating unless approved, in writing, by the Department of Public Works. The Contractor shall pay costs.  See individual Sections for temperature/humidity limits. Temporary H methods shall comply with OSHA regulations and other applicable codes, statutes, rules and regulations and shall be approved by the Department of Public Works.

### Permanent air handling equipment, when used for temporary heating, shall be equipped with disposable "construction" filters. The construction filters shall have an average efficiency at least equal to the filters specified under Division 15, but not less than 30% when tested in accordance with ASHRAE 52-76. The filters shall have an average arrestance of not less than 90% efficiency on one (1) micron size particles. Before turning over the system for final acceptance, the contractor shall remove and dispose of the construction filters; spray clean the heating and cooling coils, and drain pans to "like new" condition; and install the filters specified in Division 15.

OR

If work involves an existing facility, the following may be used if approved by the Agency.

### The General Contractor may use the existing heating system with temporary extensions, radiators or unit heaters, but such use is subject to the Owner's approval.  Coordinate use of existing facilities with Owner. Provide additional, temporary extensions and units to satisfy the criteria given in the preceding paragraph.  Owner will pay cost of energy used.  Take measures to conserve energy.  At the termination of construction, return the facilities to their original condition.  Before operation of permanent facilities, verify that installation is approved for operation and that filters are in place.

OR

If applicable to the project, and if steam is available, use the following.

### Steam from the Agency's lines shall be metered and paid for by the Contractor at a price approved by the Agency and Department of Public Works.  The Contractor shall arrange with his Heating Subcontractor to install and maintain temporary piping, radiators, or unit heaters, reducing valves, steam traps and other necessary fittings and accessories.  Traps shall be provided to prevent steam from entering main returns.  The temporary layout shall meet the approval of the Architect/Engineer.  Condensate meter (or meters) shall be installed to record usage of steam.  (The following sentence  shall be used when steam is supplied free:  "Steam from the Agency's lines will be furnished to the Contractor without cost, but may be discontinued if use is unreasonable or wasteful".)  At the termination of construction, return the facilities to their original condition.

## 01515	TEMPORARY TELEPHONE

### General Contractor shall provide telephone service in his office and a separate telephone in the Department of Public Works Field Office, if provided.  It is preferred the Contractor use a cellular phone. Local calls will be paid by the Contractor and toll calls by the respective users.

OR

In existing facilities, coordinate with the Owner, and, if applicable, use the following:

### A.	Pay phones are available at the existing facility; the Contractor may use this equipment.

OR

### Public pay phones are not available at the existing facility, but the Agency, with prior notification, will make a phone available for local calls.  All pay calls shall be logged and paid by the Contractor.

## 01520	TEMPORARY WATER

### Water for construction purposes may be taken from the existing service. The Contractor shall provide connections, approved backflow prevention device, meter and pipe to the water main or nearest hydrant, subject to the approval of the Department of Public Works.  Upon completion of work, the Contractor shall remove the temporary connections and backfill if necessary.  If new water service is installed before construction is complete, the new system may be used provided it is returned to the Owner in as-new condition.  The Contractor shall pay for the water used, as metered.

OR

Where water is not available on site, use the following:

### Water is not available on site.  Transport water to the project.  Cost shall be paid by the General Contractor.

OR

If Owner will pay for water, use the following:

### Connect to existing facilities, through an approved backflow prevention device; extend branch piping with outlets so that water is available by use of hoses.  Owner will pay for water used.  The Contractor shall not waste water or use faulty equipment.  The Contractor shall provide, at his own expense, all connections, extensions and other apparatus required for use of such services.  Upon completion of the Contract, the Contractor shall disconnect temporary extensions and return utility to its original condition.

## 01525	TEMPORARY SANITARY FACILITIES

### The Contractor shall provide, where directed, chemical toilets with toilet tissue, plus wash basins with water, soap and paper towels.  The Contractor shall maintain the facilities in a sanitary condition.

### If women are employed in the work, provide separate, designated facilities for them of the same kind.  Provide an adequate number of each kind of facility for each gender.

OR

Specifier:  When project involves an existing facility, coordinate with the Agency for possible use of existing toilets.

### Designated existing toilets may be used during construction.  It is the responsibility of the Contractor to maintain the facilities in a clean and sanitary condition and return them to their original condition after use.  No loitering or smoking  will be permitted in these areas.

## 01530	FIRE PROTECTION

### The Contractor, during construction, shall be responsible for loss or damage by fire to the work of the Contract until completion.  Any fire used within the structure for working purposes shall be extinguished when not in use.  Bitumen or tar shall be melted on the ground only. No flammable material shall be stored in the structure in excess of amounts allowed by the authorities.  No gasoline shall be stored in or close to the building at any time.  The Contractor shall assign a responsible employee to be in charge of fire protection measures.

### If an EPDM or other single-ply roof is included in the work that requires cleaning of mating surfaces of laps with gasoline, limit amount of gasoline on roof to 2 gallons which shall be in U.L. listed containers.  Also provide one 30 B:C fire extinguisher within 75 feet of any point on the roof.

## 01535	CONSTRUCTION EQUIPMENT

### The Contractor shall furnish tools, apparatus and appliances, hoists and/or cranes and power for same, scaffolding, runways, ladders, temporary supports and bracing and similar work or material necessary to insure convenience and safety in the execution of the Contract except where this is otherwise specified in any Specification Section.  All such items shall meet the approval of the Department of Public Works but responsibility for design, strength and safety shall remain with the Contractor.  All such items shall comply with Federal OSHA regulations and applicable codes, statutes, rules and  regulations, including compliance with the requirements of the current edition of the "Manual of Accident Prevention in Construction" published by the A.G.C. and the standards of the State Labor Department.

### Staging, exterior and interior, required for the execution of this Contract, shall be furnished, erected, relocated if necessary and removed by the General Contractor.  Staging shall be maintained in a safe condition without charge to and for the use of all trades as needed.

## 01540	BARRIERS AND ENCLOSURES

### Provide barriers to prevent public entry into construction areas and to protect existing facilities from damage by construction operations.

### Provide a fence around construction site; equip with vehicular and pedestrian gates with locks.

### Provide covered walkways as required by governing authorities for public rights-of-way and for public access to existing  buildings.

### Provide barriers around trees and plants designated to remain.  Protect against vehicular traffic, materials' dumping, chemically injurious materials, puddling or running water.

### Provide temporary, insulated, weathertight closures at openings to the exterior to provide acceptable working conditions and protection for materials, to allow for temporary heating and to prevent entry of unauthorized persons.  Provide doors with self-closing hardware and locks.

### Barriers and enclosures shall be in conformance with code requirements. Do not block egress from occupied buildings unless necessary to further the work of the Contract.  In this case, secure the Department's approval of an alternate egress plan.

### See also General Conditions Article 19 “Protection of the Work, Persons and Property”.

## 01545	PROTECTION

### Protect buildings, equipment, furnishings, grounds and plantings from damage.  Any damage shall be repaired or otherwise made good at no expense to the State.

### Provide protective coverings and barricades to prevent damage.  The Contractor shall be held responsible for, and 	must make good at his own expense, any water or other type of damage due to improper coverings. Protect the public and building personnel from injury.

### Provide temporary protection for installed products.  Control traffic in immediate area to minimize damage.

### Provide protective coverings for walls, projections, jambs, sills and soffits of openings.  Protect finished floors and stairs from traffic, movement of heavy objects and storage.  Prohibit traffic and storage on waterproofed and roofed surfaces and on lawn and landscaped areas.

Specifier:  For alterations & additions to existing facilities add:

### Provide temporary partitions and ceilings to separate work areas from Owner-occupied areas to prevent penetration of dust and moisture into Owner-occupied areas and equipment.  Erect framing and sheet materials with closed joints and sealed edges at intersections with existing surfaces.

### See also General Conditions Article 19 “Protection of the Work, Persons and Property”.

## 01550	SECURITY

### Provide security program and facilities to protect work, existing facilities and Owner's operations from unauthorized entry, vandalism and theft.  Coordinate with Owner's security program.

### The Contractor shall be solely responsible for damage, loss or liability due to theft or vandalism.

## 01555	TRAFFIC WAYS

### The Contractor may use on-site paved roads and parking areas but shall not encumber same or their access.  Public highways shall not be blocked by standing trucks, parked cars, material storage, construction operations or in any other manner.

### Public roads and existing paved roads, drives and parking areas on Owner's property shall be kept free from scrap or debris due to construction operations and any damage to their surface caused by the Contractor shall be repaired by him at his own expense.

### If the work of the Contract affects public use of any street, road, highway or thoroughfare, the G. C. shall confer with the police authority having jurisdiction to determine if and how many police are needed for public safety in addition to any barriers and signals that may be needed. The G.C. will be responsible for payment of any needed police services.

## 01560	TEMPORARY CONTROLS

NOTE:  Delete paragraph below only when cost considerations are paramount.  Expand if specific pests, such as termites or pigeons, are known to be a problem.

Refer to governing codes, such as OSHA, EPA and USDA covering most temporary environmental controls.  However, work involving alterations and additions may require more specific job-related controls; the following are examples. Confer with  Project Manager for specifics.

Edit as required.

### Temporary Environmental Controls:  Contractor is to provide the following controls.

#### Rodent and Pest Control: Before deep foundation work has been completed, retain a local exterminator or pest control company to recommend practices to minimize attraction and harboring of rodents, roaches, and other pests.  Employ this service to perform extermination and control procedures at regular intervals so the Project will be free of pests and their residues at materials.

#### Dust Control (construction and demolition).

#### Noise Control.

#### Erosion and Sediment Control.

#### Pollution Control.

#### Traffic Control.

## 01565	STORM WATER CONTROL

This section to be used when a Stormwater Pollution Permit is required, otherwise delete. Consult with Project Manager.

### Assume responsibility for Storm Water pollution control by submitting to the Connecticut Department of Environmental Protection (DEP) a "General Permit for the Discharge of Storm Water and Dewatering Wastewaters from Construction Activities" registration; conform to the permit requirements.

### Conform to the Storm Water Pollution Control Plan included in the Contract Documents or have another plan, prepared at the General Contractor's expense, which has been approved by the Department of Public Works and Environmental Protection.

### The "General Permit for the Discharge of Storm Water and Dewatering Wastewater from Construction Activities" "draft" registration is attached to the technical Section 0227      Storm Water Pollution Control.

### Sign, and cause to be signed by each appropriate subcontractor, the Certification Statement required by the General Permit.

### Provide, maintain, and monitor a rain gauge on the site; monitoring shall include maintaining a log of the readings.  The rain gauge shall remain the property of the General Contractor.

## 01570	CLEANING

### Maintain areas under Contractor's control free of waste materials, debris and rubbish.  Maintain in a clean and orderly condition.

### Remove debris and rubbish from pipe chases, plenums, attics, crawl spaces and other closed or remote spaces before closing the space.

### Periodically clean interior areas before start of surface finishing and continue cleaning on an as-needed basis.

### Control cleaning operations so that dust and other particulates will not adhere to wet or newly-coated surfaces.

### Remove waste materials, debris and rubbish from site daily and dispose of legally off-site.  No scrap/debris shall remain inside the building or anywhere on site upon final acceptance of the project.

### See also General Conditions Article 24 “Cleaning Up”.

## 01575	PROJECT SIGNS

### Project Signs: Engage an experienced sign painter to apply graphics.  Comply with details to be furnished by the Construction Administrator.

NOTE:  Revise subparagraphs below to suit project.

#### Project Sign: The Contractor shall contact the Construction Administrator for the proper wording for the project sign.  Fabricate sign of 3/4", exterior grade, A-B Fir plywood.  Mount sign on preservative treated Fir posts.    Paint both sides and all edges of sign and the posts with two coats of exterior, white, alkyd primer.  Paint the border and letters with "bulletin" (sign) paint.  Letter sizes, colors and related information is given on the illustration as below.  A self-adhesive decal of the State seal will be furnished at the Contract signing. Erect the sign within two weeks after execution of the Contract and remove the sign within one week after completion of the project.  The Owner shall provide design, color selection and detailed illustration of the Project Sign.

## 01580	FIELD OFFICES AND SHEDS

Architect/Engineer:  This article may not be required on small projects; Check with Project Manager.

### Field Offices:

OPTION A: (select only one option)  The  subparagraph below is when a trailer is not needed for DPW or Agency. Option only used for very small projects with the approval of the Project Manager.

#### The Contractor shall provide an office for his own use which may be a trailer type facility with electric lighting, air conditioning, and heat.  It shall have ample natural light, a table, chairs, counter, shelf, plan racks and file cabinets. Provide a 5 lb. ABC fire extinguisher and an OSHA-approved first aid kit. If the contract amount is $2,500,000 or more, the Contractor shall provide a facsimile machine in his office and shall also provide his superintendent with a message beeper.

OR

OPTION B: (select only one option)  The  subparagraph below is for Agencies providing space in an existing building. Typically Projects less than $2,500,000. Add or delete items of furniture or supplies as needed.

NOTE:  Also, check with the Project Manager and Agency if the following paragraph can be used for alteration, renovation or rehabilitation projects.

#### The Agency will furnish, without charge, (1) one room(s) for the Contractor's use as an office in an existing building. The Department of Public Works Manager will share the Contractor's office. The Contractor shall provide and install a 5 lb. ABC fire extinguisher and an approved first aid kit. The Contractor shall be responsible for furniture and shall keep this area clean and return it to its original condition after use. The Contractor shall provide the following furniture, which will remain his property. The furniture may be used but shall be in good condition as judged by the Construction Administrator.

##### The contractor shall provide a lockable chemical toilet with toilet tissue for the owners’ use. The contractor shall maintain the facility in a sanitary condition.

##### (1) One lockable, double-pedestal, office desk, with an executive chair.

##### (1) One plan table.

##### (1) One plan rack.

##### (6) Six conference chairs and a conference table (approx. 3’x6’).

##### (1) One side table (approx. 3’x5’).

##### (1) One 4’x6’ wall mounted, cork display board.

##### (1) One 3’x4’ wall mounted, white, wipe-off board, with markers.

##### (2) Two file cabinets (lockable four drawer letter size).

##### (1) One bookshelf w/10 L.F. of 12" wide shelving each.

##### (1) One large capacity waste receptacle.

##### (1) One plain paper, Fax Machine with dedicated telephone line approved by Owner.

##### (2) Two telephones with telephone lines and voice mail.

##### (1) One telephone line (dedicated to computer use) with high-speed Internet connection (minimum of DSL or cable modem service).

NOTE: Insert Microsoft Project (latest version) as required by Section 01310 Construction Schedules or 01315 CPM Schedules and delete scheduling software not referenced in the schedule section utilized for the specific project. All computer software information should be verified prior to bidding each job to verify what is indicated is readily available.

##### (1) One Computer, with a 19” monitor, internet and E-mail connection capabilities and the following: 20 GB min hard-drive (7200 rpm) EIDE, the computer shall have a CDRW drive, graphic and sound cards, integrated 3com 10/100 NIC (Network Interconnection Capability), 3.5” 1.44 MB floppy disk drive, (2) serial (1) parallel and (2) USB ports, external powered speakers, CD--ROM, 1.5 GHz (minimum) Pentium IV with operating software, including but not limited to, Windows XP, AutoCAD reading program as Voloview, Microsoft Office XP Professional (with working E-mail, ISP by GC), Microsoft Project (latest version), Norton Anti-virus. All software supplied shall be compatible versions.

##### (1) One Laser printers, with (2) hub connections, with supplies approved by Owner.

##### (1) One Copy Machine with automatic stapling, coping capability for letter sized paper (8 ½ x 11), legal size (11 x 14) and ledger size (11 x 17), ability to enlarge and reduce, with collation up to 10 sets, duplex copying (both sides), and supplies for machine approved by Owner.

##### (1) One Color printer with ink and photo paper supplies (equivalent to Epson Stylus Photo 785EPX Inkjet 2880X720DPI 6 Color Full Bleed).

##### (1) One Digital Camera with software (equivalent to Olympus Camedia C-700 Ultra Zoom Digital Camera).

##### (1) One battery operated wall clock.

##### (1) One mailbox.

OR

OPTION C: (select only one option)  The  subparagraph below is for Projects typically below $10,000,000 that require a construction trailer. Add or delete items of furniture or supplies as needed.

#### The contractor shall provide a field office for the Construction Administrator and the owner. The field office shall be (1) one single wide trailer 12’ x 60’.  The trailer shall have to be in “new condition” as determined by the Construction Administrator.  The trailer shall have a minimum of two (2) offices (minimum 150 square feet each), and  a main meeting area. The trailers shall have ample natural light, heating of sufficient capacity to maintain 70 degrees (F) in winter and air conditioning of sufficient capacity to maintain 75 degrees (F) in summer.  The operational noise level of the supplied HVAC systems shall be low enough so as not to impede the conducting of meetings. The Contractor shall provide a 5-lb. ABC fire extinguisher and an OSHA- approved first aid kit. The Contractor shall provide the following furniture, which will remain his property.  The furniture may be used but shall be in good condition as judged by the Construction Administrator.

NOTE:  Revise subparagraph below by adding or deleting additional items of furniture as needed.

#### The contractor shall provide a lockable chemical toilet with toilet tissue for the owners’ use. The contractor shall maintain the facility in a sanitary condition.

#### (2) Two lockable, double-pedestal, office desks, each with an executive chair.

#### (2) Two plan tables.

#### (2) Two plan racks.

#### (10) Ten conference chairs and a conference table (approx. 5’x12’).

#### (2) Two side tables (approx. 3’x5’).

#### (2) Two 4’x6’ wall mounted, cork display boards.

#### (1) One 3’x4’ wall mounted, white, wipe-off board, with markers.

#### (4) Four file cabinets (lockable four drawer letter size).

#### (2) Two bookshelves w/10 L.F. of 12" wide shelving each.

#### (2) Two large capacity waste receptacles.

#### (1) One plain paper, Fax Machine with dedicated telephone line approved by Owner.

#### (2) Two telephones with telephone lines and voice mail.

#### (2) Two telephone lines (dedicated to computer use) with high-speed Internet connection (minimum of DSL or cable modem service).

NOTE: Insert Microsoft Project (latest version) as required by Section 01310 Construction Schedules or 01315 CPM Schedules and delete scheduling software not referenced in the schedule section utilized for the specific project. All computer software information should be verified prior to bidding each job to verify what is indicated is readily available.

#### (2) Two Computers, each with a 19” monitor, internet and E-mail connection capabilities and the following: 20 GB min hard-drive (7200 rpm) EIDE, the computers shall have a CDRW drive, graphic and sound cards, integrated 3com 10/100 NIC (Network Interconnection Capability), 3.5” 1.44 MB floppy disk drive, (2) serial (1) parallel and (2) USB ports, external powered speakers, CD--ROM, 1.5 GHz (minimum) Pentium IV with operating software, including but not limited to, Windows XP, AutoCAD reading program as Voloview, Microsoft Office XP Professional (with working E-mail, ISP by GC), Microsoft Project (latest version), Norton Anti-virus. All software supplied shall be compatible versions.

#### (1) One Laser printer, with (2) hub connections, with supplies approved by Owner.

#### (1) One Copy Machine with automatic stapling, coping capability for letter sized paper (8 ½ x 11), legal size (11 x 14) and ledger size (11 x 17), ability to enlarge and reduce, with collation up to 10 sets, duplex copying (both sides), and supplies for machine approved by Owner.

#### (1) One Color printer with ink and photo paper supplies (equivalent to Epson Stylus Photo 785EPX Inkjet 2880X720DPI 6 Color Full Bleed).

#### (1) One Digital Camera with software (equivalent to Olympus Camedia C-700 Ultra Zoom Digital Camera).

#### (1) One battery operated wall clock.

#### Window blinds.

#### (1) One mailbox.

### 3.	When the Contractor supplies the trailer(s) they shall equip each trailer with a water cooler for hot and cold water.

NOTE:  Expand paragraphs below to suit project.

### Storage and Fabrication Sheds: Install storage and fabrication sheds sized, furnished, and equipped to accommodate materials and equipment involved, including temporary utility service.  Sheds may be open shelters or fully enclosed spaces within the building or elsewhere on-site.

#### Storage sheds for tools, materials and equipment shall be weathertight with heat, lighting and ventilation for products requiring controlled conditions.

#### Remove temporary materials, equipment services and construction before Substantial Completion.

#### Clean and repair damage caused by installation or use of temporary facilities.  Restore existing facilities used during construction to specified or to original condition.

Paragraph can be used for alteration, renovation or rehabilitation projects. Check the following for use on alteration, renovation or rehabilitation projects with Project Manager.

## 01585	IDENTIFICATION BADGES

### A.	Identification Badges for Contractor's Personnel, Visitors & Parking Stickers:

#### The Contractor will provide each person working or visiting at the site with an identification badge, bearing the name of the Contractor and a number.  As badges are assigns, a record shall be kept by the Contractor and given to the Construction Administrator and Agency Administrator.  Update and correct the records of all badges issued on a semi-monthly basis.

#### Badges are to be worn on outer garment where visible at all times while at the construction site, return them to the Contractor’s field office at the end of each day and pick them up there each morning.

NOTE:  Retain paragraph below and modify if parking stickers are required for the specific project and modify if parking stickers are to be issued by the Contractor's rather than the Agency for the specific project.

#### All vehicles parking in the Contractor's parking lot and those used around the site require an ID sticker.  They will be issued by the Agency.  Each contractor shall apply for parking stickers through the Construction Administrator no more than semi-monthly and shall keep record of all stickers issued.

## 01600	MATERIALS AND EQUIPMENT CONTROLS

NOTE:  This Section 01600 "Materials and Equipment Controls” includes, but not limited to, administrative and procedural requirements governing the Contractor’s selection and use of products including but not limited to their transportation, handling, storage, and protection.  Edit paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Materials and Equipment:  Shall be delivered, stored and handled to prevent intrusion of foreign matter and damage by weather or breakage.  Packaged materials shall be delivered and stored in original, unbroken packages.

#### Promptly inspect shipments to assure that products comply with requirements, that quantities are correct and products are undamaged.

#### Packages, materials and equipment showing evidence of damage will be rejected and replaced at no additional cost to the Owner.

### Storage and Protection:

#### Store products in accordance with manufacturers' instructions with seals and labels intact and legible.  Store sensitive products in weathertight enclosures; maintain within temperature and humidity range required by manufacturer.

#### For exterior storage of fabricated products, place on sloped supports above ground.  Cover products subject to deterioration with impervious sheet covering; provide ventilation to avoid condensation.

#### Store loose granular material on solid surfaces in a well-drained area; prevent mixing with foreign matter.

#### Arrange storage to provide access for inspection.  Periodically inspect to insure products are undamaged and are maintained under required conditions.  Keep log showing date, time and problems, if any.

#### Stone, masonry units and similar materials shall be stored on platforms or dry skids and shall be adequately covered and protected against damage.

Include the following, if applicable.

#### The Contractor shall prepare, as directed by the Owner, one area or space in the building for storage of State-owned equipment.

## 01631	EQUALS AND SUBSTITUTIONS

NOTE:  The Section 01631 "Equals and Substitutions”  includes detailed procedural requirements for handling and processing requests for equals and substitutions for a product or system for a specified product or system.  INDIVIDUAL SPECIFICATION SECTIONS WHICH INDICATE THAT A PRODUCT OR SYSTEM EQUAL AND SUBSTITUTION IS PERMISSIBLE MUST REFERENCE THIS SECTION.  ”Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

NOTE:  All specification sections must list at a minimum, 3 manufacturers for all products.  The use of one named manufacturer and or equal as well as the use of a performance specification is not allowed.  All products specified in Divisions 2-17 must list the order of preference of all products, (If product no. 1 is first choice) all equals must be equivalent to the first manufacturer listed in the specific specification section.

### Definitions:  Definitions in this Article do not change or modify the meaning of other terms used in the Contract Documents.

NOTE:  Retain paragraph below.  These definitions refer specifically to contents of this section and are not repeated in division 1 section "reference standards and definitions."

NOTE:  Revise paragraph below as appropriate for multiple prime contracts or special project requirements.

#### Equals or Substitutions General:  Changes in products, materials, equipment, and methods of construction required by the Contract Documents proposed by the Contractor after award of the Contract.

#### Equal: Any deviation from the specification which is defined as follows: A replacement for the specified material, device, procedure, equipment, etc., which is recognized and accepted as substantially equal to the first listed manufacturer or first listed procedure specified, after review, by the Architect and may be rejected or approved at the sole discretion of the owner.  All equals must be substantially equivalent to the first manufacturer or first procedure listed in the Specifications with reference to all of the following areas: the substance and function considering quality, workmanship, economy of operation, durability and suitability for purposes intended; size, rating and cost.  The equal does not constitute a modification in the scope of Work, the Schedule or Architect/Engineer’s design intent of the specified material, device, procedure, equipment, etc.

#### Substitution:  Any deviation from the specified requirements, which is defined as follows:  A replacement for the specified material, device, procedure, equipment, etc., which is not recognized or accepted as equal to the first manufacturer or procedure listed in the Specification after review by the Architect and may be rejected or approved by the Owner.  The Substitution is not equal to the specified requirement in comparison to the first manufacture or first procedure listed in the Specifications in one or more of the following areas: the substance and function considering quality, workmanship, economy of operation, durability and suitability for purposes intended; size; cost and rating.  The Substitution constitutes a modification in the scope of Work, the Schedule or the Architect/Engineer’s design intent of the specified material, device, procedure, equipment, etc.

#### The following are not considered to be requests for Equals or Substitutions:

##### Revisions to the Contract Documents requested by the Owner or Architect.

##### Specified options of products and construction methods included in the Contract Documents.

##### The Contractor's determination of and compliance with governing regulations and orders issued by governing authorities having jurisdiction.

NOTE:  See definitions for “Equal Substitution” and “Unequal Substitution” in Article 1 of the General Conditions.

### Submittals:

NOTE: The “General Conditions” does not address equal substitution or substitution requests directly. The “Supplementary Conditions” reference procedures for consideration of “substitutions after contract award.  Paragraph and "substitutions" article below amplify requirements suggested by “Supplementary Conditions” ..

#### Equals and Substitution Request Submittals: The Owner will consider requests for equals or substitutions if received within time period designated in the General Conditions Article 15 “Materials; Standards”.  Requests received more than the days specified in Article 15 after the start date of the contract will be rejected.

##### The Contractor is required to prepare and submit 3 copies of the required data for the first manufacturer listed or procedure listed in the specifications section with reference to all of the following areas: the substance and function considering quality, workmanship, economy of operation, durability and suitability for purposes intended including the size, rating and cost.  All submissions must include all the required data for the first listed manufacturer or procedure as specified, as well as the required data for the proposed Equal or Substitution.  This will enable the Owner and Architect to determine that the proposed Equal or Substitution is or is not substantially equal to the first listed manufacturer or procedure.

#### Identify the product or the fabrication or installation method to be replaced in each request.  Include related Specification Section and Drawing numbers.

#### Provide complete documentation showing compliance with the requirements for equals or substitutions, and the following information, as appropriate on a “Substitution Request” form as required by the Owner:

NOTE:  Delete requirements below that are unnecessary or included in the “Supplementary Conditions”.  Modify, as necessary, retained subparagraphs to suit project.

##### Coordination information, including a list of changes or modifications needed to other parts of the Work and to construction performed by the Owner and separate contractors, that will be necessary to accommodate the proposed Equal or Substitution.

##### A detailed comparison chart of significant qualities of the proposed substitution with those of the Work specified.  Significant qualities may include elements, such as performance, weight, size, durability, and visual effect.

##### Product Data, including Shop Drawings and descriptions of products and fabrication and installation procedures.

##### Samples, where applicable or requested.

##### A statement indicating the effect on the Contractor's Construction Schedule or CPM Schedule compared to the schedule without approval of the Equal or Substitution.  Indicate the effect on overall Contract Time.

##### Cost information, broken down, including a proposal of the net change, if any in the Contract Sum.

##### The Contractor's certification that the proposed Equal or Substitution conforms to requirements in the Contract Documents in every respect and is appropriate for the applications indicated.

##### The Contractor's waiver of rights to additional payment or time that may subsequently become necessary because of the failure of the Equal or Substitution to perform adequately.

NOTE:  Revise subparagraph below if necessary to allow more time to the 2 weeks and two week approval and re-submittal process requests.

#### Architect's Action: If necessary, the Architect will request additional information or documentation for evaluation within one week of receipt of the original request for equal or substitution request.  The Architect will notify the Construction Administrator who will notify the Owner of recommended acceptance or rejection of the proposed equal or substitution, within two (2) weeks of receipt of the request, or one (1) week of receipt of additional information or documentation, whichever is later.  The Construction Administrator will give final acceptance or rejection by the Owner not less than one (1) week after notification.

##### Any request deemed an "Equal" and accepted by the Construction Administrator, Architect, Owner, and Agency will result in written notification to the Contractor and will not be in the form of a change order for an "Equal”.

##### Any request deemed a "Substitution" and rejected or approved by Construction Administrator, Architect, and Owner may result in written notification to the Contractor and may be in the form of a change order if the “Substitution” is approved.

### Equal or Substitutions:

#### Conditions:  The Architect will consider the Contractor's request for Equal or Substitution of a product or method of construction when one or more of the following conditions are satisfied, as determined by the Architect.  If the following conditions are not satisfied, the Architect will return the requests to the Construction Administrator without action except to record noncompliance with these requirements.

NOTE:  Delete or modify conditions below that are not acceptable.  If desired, insert more restrictive conditions to limit consideration of proposed substitutions.

##### The proposed request does not require extensive revisions to the Contract Documents.

##### The proposed request is in accordance with the general intent of the Contract Documents.

##### The proposed request is timely, fully documented, and/or properly submitted.

##### The proposed request can be provided within the Contract Time.  However, the Architect will not consider the proposed request if it is a result of the Contractor’s failure to pursue the Work promptly or coordinate activities properly.

##### The proposed request will offer the Owner a substantial advantage, in cost, time, energy conservation, or other considerations, after deducting additional responsibilities the Owner must assume.  However, if the proposed request requires the Owner to incur additional responsibilities, including but not limited to, additional compensation to the Architect for redesign and evaluation services, increased cost of other construction by the Owner or similar considerations, then the Owner will have just cause to reject the request for Equal or Substitution.

##### The proposed request can receive the necessary approvals, in a timely manner, required by governing authorities having jurisdiction.

##### The proposed request can be provided in a manner that is compatible with the Work as certified by the Contractor.

##### The proposed request can be coordinated with the Work as certified by the Contractor.

##### The proposed request can uphold the warranties required by the Contract Documents as certified by the Contractor.

#### The Contractor's submission and the Architect's review of Submittals, including but not limited to, Samples, Manufacturer’s Data, Shop Drawings, or other such items, which are not clearly identified as a request for an Equal or Substitution, will not be considered or accepted as a valid request for an Equal or Substitution, nor does it constitute an approval.

## 01650 STARTING OF SYSTEMS

NOTE:  The Section 01650 "Starting of Systems” includes detailed procedural requirements for building system start up and system demonstration.  Provide direct reference to individual product specification sections.   ”Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### General:

#### Coordinate schedule for start-up of various equipment and systems.

NOTE:  Insert the required number of day for notification prior to start-up of any systems.

#### Provide written notification the Construction Administrator thirty (30) Calendar Days prior to start-up of each item.

#### Verify that each piece of equipment or system has been checked for proper lubrication, drive rotation, belt tension, and control sequence for other conditions that may cause damage.

#### Verify that tests, meter readings, and specified electrical characteristics agree with those required by the equipment or system manufacturer.

#### Verify in wiring and support components are complete and tested.

NOTE  Include paragraphs below if it is considered an advantage of requiring the contractor to have the manufacturers field services in relationship to scope and complexity of project.  Edit or delete paragraphs that are not applicable to project.

#### Execute the start-up under supervision of manufacturer’s representative, in accordance with manufacturer’s instructions.

#### When referenced in individual specification sections, require manufacturer to provide an authorized representative to be present at the site to inspect, check, and approve equipment or system installation prior to start-up, and to supervise placing equipment or system in operation.

NOTE  Section 01400 “Quality Control” describes administrative procedures associated with the following paragraph.

#### Submit a written report in accordance Section 01400 “Quality Control” that the equipment or system has been properly installed and is functioning properly.

### Demonstration and Instructions:

NOTE:  Revise subparagraph below if necessary to allow more or less time to than the 2 weeks notification specified.

#### Demonstrate operation and maintenance of Products to Owner and Agency Personnel two (2) weeks prior to substantial completion.

NOTE:  Revise any requirements in paragraph below for special classroom instruction as appropriate for project.

#### Demonstrate Project equipment and instruct in a classroom environment at location designated by the Construction Administrator and instructed by a qualified manufacturer’s representative who is knowledgeable about the project.

#### For equipment or systems requiring seasonal operation perform demonstration for season within six (6) months.

#### Utilize operation and maintenance manuals as basis for instruction.  Review contents of manual with Owner and Agency Personnel in detail to explain all aspects of operation and maintenance.

#### Demonstrate start-up, operation, control, adjustment, troubleshooting, servicing, and maintenance, and shutdown of each item at agreed upon scheduled time and at equipment or designated location.

#### Prepare and insert additional data in operations and maintenance manuals when need for additional data becomes apparent during demonstration.

NOTE:  Consider adding special requirements that exceed those specified.  Possibilities include videocassette recordings for instruction of the owner's personnel.

### Testing Adjusting, and Balancing:

#### The Contractor will employ and pay for the testing services of an independent consultant to verify the testing, adjusting, and balancing.

#### Reports will be submitted by the independent testing consultant to the Construction Administrator indicating observations and results of tests and indicating compliance or non-compliance with the requirements of the Contract Documents.

#### The Owner may employ and pay for the services of an independent consultant to verify testing, adjusting, and balancing which was performed by the Contractor.

## 01700	CONTRACT CLOSEOUT

NOTE:  This Section 01700 "Contract Closeout” includes requirements regarding contract closeout procedures, final cleaning, adjusting. Project records, operation and maintenance data, warranties.  Revise paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Substantial Completion:

#### Preliminary Procedures: Before requesting inspection for Certification of Substantial Completion, complete the following.  List exceptions in the request.

NOTE:  Delete items from list below that are not applicable or modify items retained to suit project.

##### In the Application for Payment that coincides with, or first follows, the date Substantial Completion is claimed, show 100 percent completion for the portion of the Work claimed as substantially complete.

###### Include supporting documentation for completion as indicated in these Contract Documents and a statement showing an accounting of changes to the Contract Sum.

###### If 100 percent completion cannot be shown, include a list of incomplete items, the value of incomplete construction, and reasons the Work is not complete.

##### Advise the Owner of pending insurance changeover requirements.

##### Submit specific warranties, workmanship bonds, maintenance agreements, final certifications, and similar documents.

##### Obtain and submit releases enabling the Owner unrestricted use of the Work and access to services and utilities.  Include occupancy permits, operating certificates, and similar releases.

NOTE:  Delete subparagraph below if submittal of this material is delayed until final acceptance.

##### Submit record drawings, maintenance manuals, damage or settlement surveys, property surveys, and similar final record information.

##### Deliver tools, spare parts, extra stock, and similar items.

##### Make final changeover of permanent locks and transmit keys to the Owner.  Advise the Owner's personnel of changeover in security provisions.

##### Demonstration, thru operation and testing, the functions of all systems and/or equipment to the satisfaction of the Owner for compliance to the contract.  Complete testing of systems, and instruction of the Owner's operation and maintenance personnel.  Discontinue and remove temporary facilities from the site, along with mockups, construction tools, and similar elements.

NOTE:  Delete 2 subparagraphs below if project does not include these items or if they are delayed until final acceptance.

##### Complete final cleanup requirements, including touchup painting.

##### Touch up and otherwise repair and restore marred, exposed finishes.

NOTE:  Modify paragraph below to comply with Department of Public Works policy and project requirements.

#### Inspection Procedures: The Contract shall be ready and prepared when they request a Substantial Completion inspection.  If the inspection reveals that the work is not complete, there are extensive punchlist items and as the items listed above are not complete, the Construction Administrator, Architect, and Owner will determine the inspection has failed.

#### The Contractor is responsible for all costs to re-inspect due to a failed inspection.  The Owner will issue a deduct change order to cover all costs for re-inspection.

##### The Architect will repeat inspection when requested and assured that the Work is substantially complete.

##### Results of the completed inspection will form the basis of requirements for final acceptance.

### Final Acceptance:

#### Preliminary Procedures: Before requesting final inspection for certification of final acceptance and final payment, complete the following.  List exceptions in the request.

NOTE:  If Supplementary Conditions are added to the General Conditions then revise subparagraphs below as necessary.

##### Submit the final payment request with releases and supporting documentation not previously submitted and accepted.  Include insurance certificates for products and completed operations where required.

##### Submit an updated final statement, accounting for final additional changes to the Contract Sum.

##### Submit a certified copy of the Architect's final inspection list of items to be completed or corrected, endorsed and dated by the Architect.  The certified copy of the list shall state that each item has been completed or otherwise resolved for acceptance and shall be endorsed and dated by the Architect.

##### Submit final meter readings for utilities, a measured record of stored fuel, and similar data as of the date of Substantial Completion or when the Owner took possession of and assumed responsibility for corresponding elements of the Work.

##### Submit consent of surety to Final Payment.

##### Submit evidence of final, continuing insurance coverage complying with insurance requirements.

NOTE:  Modify paragraph below to comply with Department of Public Works policy and project requirements.

#### Reinspection Procedure: The Inspection Group will re-inspect the Work upon receipt of notice from the Construction Administrator that the Work, including inspection list items from earlier inspections, has been completed, except for items whose completion is delayed under circumstances acceptable to the Owner.

##### Upon completion of reinspection, the Construction Administrator will prepare a certificate of final acceptance.  If the Work is incomplete, the Construction Administrator will advise the Contractor of Work that is incomplete or of obligations that have not been fulfilled but are required for final acceptance.

### As Built Document Submittals:

#### General:  Do not use record documents for construction purposes.  Protect Record Documents from deterioration and loss in a secure, fire-resistant location.  Provide access to record documents for the Architect's reference during normal working hours.  Keep documents current; do not permanently conceal any work until required information has been recorded. Failure to keep documents current is sufficient cause to withhold progress payments.

##### The Contractor shall also hire the services of a Surveyor registered in the State of Connecticut to conduct a final survey to determine the location of exterior underground utility lines and to record the results, and update existing electronic media

##### The record of exterior underground utilities shall be made at the time of installation on Mylar film drawing and AutoCAD (latest version) compatible disks.  The drawing shall bear the seal of the Land Surveyor and a statement of accuracy.

#### As-built Drawings: The Contractor shall maintain one clean, complete undamaged set of blue or black line white-prints of Contract Drawings and Shop Drawings.  Mark the set to show the actual installation where the installation varies substantially from the Work as originally shown.  Mark which drawing is most capable of showing conditions fully and accurately.  Where Shop Drawings are used, record a cross-reference at the corresponding location on the Contract Drawings.  Give particular attention to concealed elements that would be difficult to measure and record at a later date.

##### Mark record sets with erasable pencil to distinguish between variations in separate categories of the Work.

##### Mark all new information that is not shown on Contract Drawings.

##### Note related change-order numbers where applicable.

##### Organize record drawing sheets into manageable sets.  Bind sets with durable-paper cover sheets; print suitable titles, dates, and other identification on the cover of each set.

##### Upon completion of the work, the Contractor shall submit Record Drawings to the Construction Administrator for the Owner's Records who will pass them on to the Architect or Engineer for transferring the changes to the Record Drawing Mylar Tracings.

##### Submit electronic format data of all Coordination Drawings as required by the owner, at no additional cost.

NOTE:  Include paragraph below if fire alarm system testing is required in the project.

##### Refer to Section 01400 “Quality Control” Section 1.3 for required as built drawings and specifications for fire alarm systems.

NOTE:  Consider deleting paragraph below on small projects.

#### Record Specifications: The Contractor shall maintain one complete copy of the Project Manual, including Addenda.  Include with the Project Manual one copy of other written construction documents, such as Change Orders and modifications issued in printed form during construction.

##### Mark these documents to show substantial variations in actual Work performed in comparison with the text of the Specifications and modifications.

##### Give particular attention to equals and substitutions and selection of options and information on concealed construction that cannot otherwise be readily discerned later by direct observation.

##### Note related record drawing information and Product Data.

##### Upon completion of the Work, submit record Specifications to the Construction Administrator for the Owner's records.

NOTE:  Consider deleting paragraph below on small projects.  If change-order proposals include resubmittal of updated product data, the need to mark up the previous submittal is eliminated.

#### Record Product Data: The Contractor shall maintain one copy of each Product Data submittal.  Note related Change Orders and markup of record drawings and Specifications.

##### Mark these documents to show significant variations in actual Work performed in comparison with information submitted.  Include variations in products delivered to the site and from the manufacturer's installation instructions and recommendations.

##### Give particular attention to concealed products and portions of the Work that cannot otherwise be readily discerned later by direct observation.

##### Upon completion of markup, submit complete set of Record Product Data to the Construction Administrator for the Owner's records.

NOTE:  Paragraph below represents the normal disposition of samples. Revise as required.

#### Record Sample Submitted: Immediately prior to Substantial Completion, the Contractor shall meet with the Construction Administrator, Architect and the Owner's personnel at the Project Site to determine which Samples are to be transmitted to the Owner for record purposes.  Comply with the Owner's instructions regarding delivery to the Owner's Sample storage area.

NOTE:  Paragraph below contains requirements for handling miscellaneous record submittals, such as foundation depths, special measurements, tests, surveys, mix records, and inspections by government authorities.  If more detailed requirements are necessary, add a summary of miscellaneous record submittals.

#### Miscellaneous Record Submittals: Refer to other Specification Sections for requirements of miscellaneous record keeping and submittals in connection with actual performance of the Work.  Immediately prior to the date or dates of Substantial Completion, complete miscellaneous records and place in good order.  Identify miscellaneous records properly and bind or file, ready for continued use and reference.  Submit to the Construction Administrator for the Owner's records.

NOTE:  Revise and add or delete items from listed examples below that are not applicable or modify items retained to suit project.

#### Maintenance Manuals: Organize operation and maintenance data into suitable sets of manageable size.  Bind properly indexed data in individual, heavy-duty, 2-inch (51-mm), 3-ring, vinyl-covered binders, with pocket folders for folded sheet information.  Mark appropriate identification on front and spine of each binder according to section 01730 “Operations & Maintenance Data”.  Included but not limited to the following types of information:

##### Emergency instructions.

##### Spare parts list.

##### Copies of warranties.

##### Wiring diagrams.

##### Recommended "turn-around" cycles.

##### Inspection procedures.

##### Shop Drawings and Product Data.

##### Fixture lamping schedule.

### Closeout Procedures:

NOTE:  Retain paragraph below unless project uses Division 1 supplemental section "operation and maintenance data."

#### Operation and Maintenance Instructions: Arrange for each Installer of equipment that requires regular maintenance to meet with the Owner's personnel to provide instruction in proper operation and maintenance.  Provide instruction by manufacturer's representatives if installers are not experienced in operation and maintenance procedures.  Include a detailed review of the following items:

NOTE:  Modify list below to suit project.

##### Maintenance manuals.

##### Record documents.

##### Spare parts and materials.

##### Tools.

##### Lubricants.

##### Fuels.

##### Identification systems.

##### Control sequences.

##### Hazards.

##### Cleaning.

##### Warranties and bonds.

##### Maintenance agreements and similar continuing commitments.

NOTE:  A/E to identify video taping of demonstration.

#### As part of instruction for operating equipment, demonstrate the following procedures:

##### Startup.

##### Shutdown.

##### Emergency operations.

##### Noise and vibration adjustments.

##### Safety procedures.

##### Economy and efficiency adjustments.

##### Effective energy utilization.

### Final Cleaning:

NOTE:  Delete this article if owners prefer to use their own forces.  Cleaning provisions in the general conditions are limited to rubbish removal and similar activities.

#### General:  The General Conditions requires general cleaning during construction.  Regular site cleaning is included in Division 1 Section 01570 “Cleaning”".

#### Employ experienced workers or professional cleaners for final cleaning.  Clean each surface or unit to the condition expected in a normal, commercial building cleaning and maintenance program.  Comply with manufacturer's instructions.  Complete the following cleaning operations before requesting inspection for Certification of Substantial Completion and Certification of Occupancy.

NOTE:  Below is a sample list of final-cleaning requirements.  Modify to suit project.  If list is extensive, use Division 1 supplemental section "final cleaning."

#### Interior:

##### Remove labels that are not permanent labels.

##### Clean transparent materials, including mirrors and glass in doors and windows.  Remove glazing compounds and other substances that are noticeable vision-obscuring materials.  Replace chipped or broken glass and other damaged transparent materials. Remove paint spots; wash and polish glass

##### Clean exposed interior hard-surfaced finishes to a dust-free condition, free of stains, films, and similar foreign substances.  Restore reflective surfaces to their original condition.  Leave concrete floors broom clean.  Vacuum carpeted surfaces.

##### Wash washable surfaces of mechanical, electrical equipment and fixtures and replace filters, clean strainers on mechanical equipment.  Remove excess lubrication and other substances.  Clean plumbing fixtures to a sanitary condition.  Clean light fixtures and lamps.

##### Clean and polish finish hardware.

##### Clean and polish tile and other glazed surfaces.

##### Clean floors; wax and buff resilient tile.  Clean vinyl or rubber base.

##### Vacuum and/or dust walls, ceilings, lighting fixtures, ceiling diffusers and other wall and ceiling items.

##### Remove defacements, streaks, fingerprints and erection marks.

#### Exterior:

##### Clean the site, including landscape development areas, of rubbish, litter, and other foreign substances.  Sweep paved areas broom clean; remove stains, spills, and other foreign deposits.  Rake grounds that are neither paved nor planted, to a smooth, even-textured surface.

##### Clean exposed exterior hard-surfaced finishes to a dust-free condition, free of stains, films, and similar foreign substances.

##### Clean roofs, gutters and downspouts.

##### Remove waste and surplus materials, rubbish and construction equipment and facilities from the site, and deposit it legally elsewhere.

##### Clean transparent materials, including mirrors and glass in doors and windows.  Remove glazing compounds and other substances that are noticeable vision-obscuring materials. Replace chipped or broken glass and other damaged transparent materials. Remove paint spots; wash and polish glass.

NOTE:  First two paragraphs below represent the end of work specified in Division 1 Section 01560" Temporary Controls."  Most projects require these actions at completion of construction.  Insert a paragraph on termite inspection where required for specific project.

#### Pest Control:  Engage an experienced, licensed exterminator to make a final inspection and rid the work of rodents, insects, and other pests.

#### Removal of Protection: Remove temporary protection and facilities installed for protection of the Work during construction.

#### Compliance:  Comply with regulations of authorities having jurisdiction and safety standards for cleaning.  Do not burn waste materials.  Do not bury debris or excess materials on the Owner's property.  Do not discharge volatile, harmful, or dangerous materials into drainage systems.  Remove waste materials from the site and dispose of lawfully.

##### Where extra materials of value remain after completion of associated Work, they become the Owner's property.  Dispose of these materials as directed by the Construction Administrator.

##### Leave building clean and ready for occupancy.  If the Contractor fails to clean up, the Owner may do so, with the cost charged to the Contractor.  The Owner will issue a credit change order to cover the costs.

NOTE:  Consider adding an article on continuing inspections or consultations by the contractor.  Possibly insert a schedule of approximate times for inspections.

## 01730	OPERATION AND MAINTENANCE DATA

NOTE:  This Section 01730 "Operation and Maintenance Data” includes administrative and procedural requirements for preparing and submitting operation, instruction, and maintenance manuals.  Edit paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### The Contractor shall instruct the State's designated personnel in the operation of new equipment and shall provide manuals and if required, provide video tapes of this basic maintenance of the equipment for training purposes. Provide qualified personnel for as long as necessary to instruct the State's personnel.

### Submit four copies of the manuals in 3-ring, loose-leaf notebooks to the Architect/Engineer for approval.  Manuals may consist of plain paper copies of approved shop drawings and catalog cuts.  Upon completion and approval, 3 copies will be forwarded to the State and one copy retained by the Architect/Engineer.

### Manuals shall include:

#### Operating Procedures:

##### Typewritten procedures for each mode of operation of each piece of equipment.  Procedures shall indicate the status of  each component of a system in each operating mode.

##### Procedures shall include names, symbols, valve tags, circuit numbers, schematic wiring diagrams, locations of thermostats, manual starters, control cabinets and other controls of each system.

### Emergency shut-down procedures for each piece of equipment or system, both automatic and manual, as appropriate.

#### Maintenance Schedule:

##### Typewritten schedule describing manufacturers schedule of maintenance and maintenance procedures.

#### Catalog Cuts:

##### To illustrate each piece of installed equipment, including options.

##### Include equipment descriptions including physical, electrical and mechanical; performance characteristics; installation or erection diagrams.

##### Include spare parts numbers and names, address and phone number of manufacturer; name, address and phone number of local representative or service department.

##### Typewritten list of all subcontractors on the project, including  name, address and phone number of local representative or service department.

#### Manuals shall be indexed with dividers indicating each system or piece of equipment.

Other uses of this medium might wish to be considered, such as a walk through of the facility prior to its completion.  An example would be a video taping of all work above the ceiling which can reveal the location of all ductwork, piping, valve locations, filter locations, etc. before the installation of the ceiling.  Walk through of crawl spaces and other areas which might be difficult to see in the buildings final completion.

## 01740	WARRANTIES AND GUARANTEES

NOTE:  This Section 01740 "Warranties and Bonds” includes administrative and procedural requirements for warranties and bonds as required by the Contract Documents, including manufacturers standard warranties on products and special warranties.  Edit paragraphs carefully to reflect specific project requirements, or delete them if they do not apply.

### Disclaimers and Limitations:  Manufacturer's disclaimers and limitations on product warranties do not relieve the Contractor of the warranty on the Work that incorporates the products.  Manufacturer's disclaimers and limitations on product warranties do not relieve suppliers, manufacturers, and subcontractors required to countersign special warranties with the Contractor.

NOTE:  Retain paragraph below.  Insert allowable exceptions here or in individual sections.

### Related Damages and Losses:  When correcting failed or damaged warranted construction, remove and replace construction that has been damaged as a result of such failure or must be removed and replaced to provide access for correction of warranted construction.

NOTE:  Modify paragraphs below as necessary to establish requirements to reinstate the warranty after failure.  Consult the Project Manager and AG when in doubt.  The original warranty starts on the date of substantial completion.  See Supplementary Conditions.  Indicate exceptions to these requirements in individual sections.  Check each warranty for special extensions.

### Reinstatement of Warranty:  When Work covered by a warranty has failed and been corrected by replacement or rebuilding, reinstate the warranty by written endorsement.  The reinstated warranty shall be equal to the original warranty with an equitable adjustment for depreciation.

NOTE:  On advice of the Project Manager and AG, expand requirement below to provide proportional cost sharing, depending on when the item failed during its useful life.  Specify exceptions in individual sections.

### Replacement Cost: Upon determination that Work covered by a warranty has failed, replace or rebuild the Work to an acceptable condition complying with requirements of the Contract Documents.  The Contractor is responsible for the cost of replacing or rebuilding defective Work regardless of whether the Owner has benefited from use of the Work through a portion of its anticipated useful service life.

### Owner's Recourse: Expressed warranties made to the Owner are in addition to implied warranties and shall not limit the duties, obligations, rights, and remedies otherwise available under the law.  Expressed warranty periods shall not be interpreted as limitations on the time in which the Owner can enforce such other duties, obligations, rights, or remedies.

#### Rejection of Warranties: The Owner reserves the right to reject warranties and to limit selection to products with warranties not in conflict with requirements of the Contract Documents.

NOTE:  Retain paragraph below.  It may make the Owner's position more secure if compromises are necessary and set the stage for recovery in the event of product failure.

### Where the Contract Documents require a special warranty, or similar commitment on the Work or part of the Work, the Owner reserves the right to refuse to accept the Work, until the Contractor presents evidence that entities required to countersign such commitments are willing to do so.

### The Contractor shall guarantee all materials and workmanship for a period of eighteen months from the date of acceptance of the Work.  In addition, the Contractor shall furnish the warranties listed below.  Submit four copies of each to the Construction Administrator in the supplier's standard form or in the form given below if there is no standard form available.

### The Contractor shall guarantee all materials and workmanship for a period of eighteen months from the date of acceptance of the Work.  In addition, the Contractor shall furnish the warranties listed below.  Submit four copies of each to the Construction Administrator in the supplier's standard form or in the form given below if there is no standard form available.

NOTE:  Edit the following to suit the subject project. Identify each Section with the 5-digit number used in each case. The list gives the minimum acceptable warranty and/or guaranty and/or terms; each is to included in the Specification Section       indicated.

#### Section 03      , Floor hardener:  5-year, material and workmanship.

#### Section 05     , Expansion Joint Covers:  5-year material & workmanship.

#### Section 07     , Single-Ply Membrane Roofing, Base Flashing and Insulation:  10-year unlimited, materials and installation: 15-year,  material and workmanship. Also, 2-year Contractor's warranty for installation.

#### Section 07     , Built Up Roofing (BUR), Base Flashing, Insulation:  20-year material and workmanship. Also 2-year Contractor's warranty for installation.

#### Section 07     , Metal Roofing and Siding:  20-year against rupture, cracks or perforation due to corrosion.  Also, 20-year for fluorocarbon finish (if used) against peeling, blistering, fading and chalking as limited by industry standards. Plus 10-year weathertightness warranty by installer.

#### Section 07     , Copper or Lead-Coated Copper Roofing:  10-year against rupture, cracks or perforation due to corrosion and including materials and workmanship.

#### Section 07     , Skylights, Vents and Hatches:  5-year product and installation, including weathertightness.

#### Section 07     , Waterproofing:  5-year material and workmanship.

#### Section 07     , Water Repellent; the term offered for the Specific product.

#### Section 07     , Exterior Expansion Joint Covers:  5-year material and workmanship, including weathertightness.

#### Section 07     , Wood Shingles (roofing, siding):  10-year for material and workmanship.

#### Section 07     , Exterior - interior caulking and sealants: 5-year, material and workmanship.

#### Section 07     , Metal Flashing and Sheet Metal: 3-year, material and workmanship.

#### Section 07     , Asphalt Roof Shingles: 25-year, material pro-rated.

#### Section 07     , Asphalt Roof Shingles Installation:  15-year,  workmanship, pro-rated.

#### Section 08     , Solid Wood Core and Mineral Core doors:  Lifetime for interior doors, 5-year for exterior doors.

#### Section 08     , Overhead Doors (coiling or sectional):  5-year material and workmanship.

#### Section 08     , Closers, Locksets, Exit Bolts:  Longest term offered by manufacturer for grade/class of particular item,  material and workmanship.

#### Section 08     , Insulating glass:  10-year against failure of hermetic seal, interpane dusting or misting including replacement of unit.

#### Section 08     , Windows:  5-year material and workmanship including weathertightness.

#### Section 08     , Laminated Glass:  10-year against delamination.

#### Section 08     , Storefront/Curtain Wall:  5-year material and workmanship (insulating glass separate). Air and water infiltration and strength to specified AAMA designation.

#### Section 09     , Carpet:  10-year wear and color fastness; 3-year installation.

#### Section 10      Operable Partitions:  5-year material and workmanship.

#### Section 10     , Mirrors;  15-years against silver spoilage.

#### Section 14     , Elevators and Wheelchair Lifts:  Material workmanship, installation for 18 months.

#### Section 15     , Fuel Storage Tank: 30-years, material and installation.

#### Section 15     , Compressors and Pumps: 5-years, material and installation.

#### Section 16      , Emergency Generator Systems: 5-years, material and installation.

NOTE:  Edit the following to suit the subject project. Identify each Section with the 5-digit number used in each case. The list gives the minimum acceptable warranty and/or guaranty and/or terms; each is to included in the Specification Section       indicated.

### Submit certification that finish materials are fire rated as specified.

### Form of Guarantees and Warranties:

Commissioner

Department of Public Works

165 Capitol Avenue

Hartford, Connecticut 06106

(Project Title and Number)

I (We) hereby guarantee and warranty)

the ________________ work on the referenced project for a period of ____________ years

from ______________, 19___ against failures of workmanship and materials in accordance

with the requirements of Section ____, Page ____, Paragraph ____, of the Specifications.

| Signed |  |
| --- | --- |
| General Contractor |  |
| (or authorized agent) |  |

### Bonds shall be by approved Surety Companies, made out to the Commissioner, Department of Public Works on companies’ standard form.

### Guarantees, warranties or bonds supplied by Subcontractors, Suppliers or Manufacturers shall reference the project name, number, and location and be certified by the General Contractor to be for the product and installation on the project and must be countersigned by the General Contractor.

### Submittals:

#### Submit written warranties prior to the date certified for Substantial Completion.  If the Architect's Certificate of Substantial Completion designates a commencement date for warranties other than the date of Substantial Completion for the Work, or a designated portion of the Work, submit written warranties upon request of the Architect.

#### Forms for special warranties are included in this Section.  Prepare a written document utilizing the appropriate form, ready for execution by the Contractor, or by the Contractor, subcontractor, supplier, or manufacturer.  Submit a draft to the Owner, through the Construction Administrator, for approval prior to final execution.

##### Refer to Divisions 2 through 17 Sections for specific content requirements and particular requirements for submitting special warranties.

NOTE:  Delete paragraphs below for small projects with only a few warranties.

#### Form of Submittal:  At Final Completion compile 2 copies of each required warranty properly executed by the Contractor, or by the Contractor, subcontractor, supplier, or manufacturer.  Organize the warranty documents into an orderly sequence based on the table of contents of the Project Manual.

NOTE:  Modify paragraph below to suit project.

#### Bind warranties and bonds in heavy-duty, commercial-quality, durable 3-ring, vinyl-covered loose-leaf binders, thickness as necessary to accommodate contents, and sized to receive 8-1/2-by-11-inch (115-by-280-mm) paper.

##### Provide heavy paper dividers with celluloid covered tabs for each separate warranty.  Mark the tab to identify the product or installation.  Provide a typed description of the product or installation, including the name of the product, and the name, address, and telephone number of the Installer.

##### Identify each binder on the front and spine with the typed or printed title "WARRANTIES," Project title or name, and name of the Contractor.

NOTE:  Coordinate requirement below with Division 1 section "Contract Closeout" or "Operation And Maintenance Data."  Make certain there are sufficient copies of warranties for inclusion in the manuals.

##### When warranted construction requires operation and maintenance manuals, provide additional copies of each required warranty, as necessary, for inclusion in each required manual.

END OF DIVISION 1- GENERAL REQUIREMENTS